## Slide 1: Lecture 11: Basic Concepts of Wavefront Reconstruction Astro 289
Rebecca Jensen-Clem
February 13, 2020
Based on slides by Claire Max, Marcos van Dam, Lisa Poyneer the CfAO Summer School, and the hcipy PYWFS tutorial

## Slide 2: What is wavefront reconstruction?
Most wavefront sensors do not measure the phase directly, but instead measure the average derivative
Most wavefront correctors are used to conjugate that phase on the mirror’s surface
We must reconstruct the phase from the WFS slopes, achieving the most accurate, lowest noise estimate possible in the least amount of computation

## Slide 3: Method 1: Zonal Matrix Reconstruction
The slope vector s contains x and y slopes for all valid subapertures in the pupil
The phase ɸ contains all controllable actuators
The basis set for reconstruction is the actuators
We model the WFS measurement process as:
We can find the measurement matrix W experimentally

## Slide 4: Experimental system matrix
Poke one actuator at a time in the positive and negative directions and record the WFS centroids
Set WFS centroid values from subapertures far away from the actuators to 0

## Slide 5: Experimental system matrix
DM surface shape
WFS image
We’re left with a # pokes by # pixels matrix, which we’re calling W

## Slide 6: Method 1: Zonal Matrix Reconstruction
Given the matrix W, we can convert phases to slopes via s = W ɸ
In reality, we’ll be measuring slopes with our WFS, and we’ll want to use those slopes to estimate the phase via ɸ = W-1 s
W isn’t square, so we’ll compute the inverse using LS:
Unfortunately, WTW isn’t invertible either –- it doesn’t have full rank because the WFS is blind to some modes

## Slide 7: Method 1: Zonal Matrix Reconstruction
Two invisible modes are piston and waffle:
Instead we’ll compute the pseudo-inverse of W using singular value decomposition (SVD), giving us an expression for ɸ = W† s

## Slide 8: Singular-Value Decomposition (SVD)
If A is a square matrix, we can write:
Where is a non-zero vector (the eigenvector) and is a scalar (the eigenvalue)
If A is not square, we can equivalently compute the eigenvectors of ATA. These are called the singular vectors of A
The square roots of the eigenvalues of ATA are called the singular values of A

## Slide 9: Singular-Value Decomposition (SVD)
If W is a real m x n matrix, we can represent it as:
U is an m x m matrix while columns are the eigenvectors of WWT
Σ is an m x n diagonal matrix whose diagonal values are the singular values of W
VT is the transpose of an n x n matrix whose columns are the eigenvectors of WTW

## Slide 10: Calculating the Pseudoinverse with SVD
Given , the pseudo inverse of W is:
Where † is the pseudoinverse
The pseudoinverse of Σ is just a diagonal matrix whose diagonal elements are the reciprocal of Σ’s diagonal elements

## Slide 11: Method 1: Zonal Matrix Reconstruction
With the reconstruction matrix we found previously, we can reconstruct an example wavefront!
DM_actst= (1-leakage) DM_actst-1 – gain(W† ⋅ WFS imaget-1)
In this “leaky integrator” example, leakage = 0.01 and gain = 0.5

## Slide 12: “Slaved” actuators
Some actuators are located outside the pupil and do not directly affect the wavefront
They are often “slaved” to the average value of its neighbors

## Slide 13: Method 2: Modal Matrix Reconstruction
We define an orthogonal modal basis set to represent the actuators: ⟨mk, ml⟩ = 0 for k ≠ l

## Slide 14: Examples of modal basis sets

## Slide 15: Method 2: Modal Matrix Reconstruction
We define an orthogonal modal basis set to represent the actuators: ⟨mk, ml⟩ = 0 for k ≠ l
We can analyze the phase in terms of modal coefficients with the inner product ck = ⟨ɸ, mk⟩
The phase is synthesized from the modal coefficients as
We can put the modes into rows or columns to produce the modal synthesis matrix M

## Slide 16: Method 2: Modal Matrix Reconstruction
Now, the slope measurement process is:
And the modal reconstruction is:
An advantage of modes is that they can be weighted and manipulated. E.g. we can easily remove piston, tip, and tilt from Zernike modes by zeroing the correct coefficients using matrix G:

## Slide 17: Keck II PYWFS Latency 1.41 kHz detector readout Slide credit: Sylvain Cetre
Camera exposure
Camera exposure
Frame demand 310ns
Readout: 709us
Processing: 27.44us
Software +
electronics
latency
DM
physical
latency:
250us
124us
Transfer, decoding: 171us
issue DM
command
½ exp.
Latency = 1.567 ms
Camera exposure: 709us
WF reconstruction & control don’t happen instantaneously!

## Slide 18
Perrin/Maire/GPI Data Analysis Team
See also Madurowicz+18,19
When the atmospheric coherence time is short compared with the AO system’s speed, we start to see effects like the “butterfly”

## Slide 19
NAS ESS Report 2018

## Slide 20: Predictive Wavefront Control
Several methods for predictive control have been proposed since the 1990s, e.g. Fourier predictive control (Poyneer et al. 2007, 2008) and Empirical Orthogonal Functions (Guyon & Males 2017)
Each method has a different way of computing the WF one time delay into the future based on past WF information
Each method makes different assumptions about the data and the atmosphere

## Slide 21
Guyon & Males 2017: put the n most recent wavefronts into a “history” vector h(t)
Notes: 1) A single wavefront consists of m measurements. Let’s put the last n wavefronts into a history vector:

## Slide 22
Guyon & Males 2017: find a filter F that minimizes the distance between F h(t) and the future wavefront ω(t+δt)
Notes: 2) We want to find the filter that minimizes the distance between the predicted and actual future wavefront:

## Slide 23
Matrix of History Vectors:
Matrix of “Future” Vectors: is the time lag
Guyon & Males 2017: to compute the filter F, we’ll use a “training set” of previous history vectors, D, and interpolate to find the corresponding training set P shifted one time delay later

## Slide 24
Guyon & Males 2017: use SVD to solve for the filter in terms of the training set
Notes: 2) We want to find the filter that minimizes the distance between the predicted and actual future wavefront:

## Slide 25
Guyon & Males 2017: how well does it work in a simple frozen flow simulation?

## Slide 26
Guyon & Males 2017: how well does it work in a simple frozen flow simulation?

## Slide 27
Notes: Say something about ideal case
Mention that the top isn’t crazy for real things

## Slide 29: Summary of Wavefront Reconstruction
Because most wavefront sensors don’t measure the phase directly, we must “reconstruct” the phase based on our information from the wavefront sensor
Usually, WF reconstruction is done with a matrix
  We can reconstruct the wavefront “zonally” in DM actuator space or “modally” e.g. in Zernike modes
  We typically measure the interaction matrix experimentally
  We compute the pseudo-inverse of the interaction matrix to find the reconstruction matrix
Predictive WFC is motivated by the time delay between reconstructing the phase and correcting the WF with the DM (often a few milliseconds or less)