## Slide 1: High-Energy Astronomy
Definitions: x-rays
0.1 Kev 1Kev 10 Kev 100Kev
3x1016hz 3x1017hz 3x1018hz 3x1019hz
124Å 12.4Å 1.24Å 0.124Å
“soft” ----------------------------- “hard”

## Slide 2: Sources
Stellar coronae (kbT~106K)
Accretion disks of binaries
AGN (non-thermal)
SN remnants (cooling of shocked gas)
Diffuse hot gas (106 - 108K) in gE galaxies, groups and clusters

## Slide 3: Focusing X-rays
X-rays penetrate glass, weird things happen at the surface of metals.
Use the concept of total internal reflectance utilizing the odd fact that n<1 for wavelengths < 2000Å and some conducting materials.
Density in gm/cm3 photon energy in keV

## Slide 4
Surfaces need to be very good and very clean
For CHANDRA, the small-scale smoothness is about 5 iridium atoms RMS…
Angles are small leading to long focal lengths, dense surfaces are better (Au, Ir), second pass of grazing incidence is useful to decrease focal length.
Field is an annulus, so use a nested mirror arrangement.

## Slide 6: Detectors
Gas Proportional Counters are the basis of traditional Geiger-Mueller Counters.
Ionizing particle or photon
e-/ion pair, high voltage, collisions, amplifier, pulse detection

## Slide 7
Little energy resolution (usually just a lower energy cutoff), little background discrimination.
Multi-anode-wire versions help to localize ionization event and sort out particles from photons and give some directional information.
In the last 10 years, most missions have gone to micro-channel plates and CCDs

## Slide 8
CHANDRA MCP photon detection. OK spatial information, excellent timing information

## Slide 9
CHANDRA CCD Array

## Slide 10: Effective Area
X-ray types use the “effective area” to characterize their facilities.
Collecting area x absorption in windows/filters x detector efficiency
ROSAT effective area

## Slide 11: CCDs and Xrays
CCDs have about 100% QE for most of the xray band. Don’t need gas supply, no threshold in energy level.
Main problem is that CCDs are sensitive to low energy photons too. The solution is to use filters (polycarbonate + aluminum). These filters have some odd transmission curves.

## Slide 12
Absorption edges are the photoelectric effect.
The crossection for absorption takes a jump at the ionization energy of a particular atomic level, then decreases approximately like -3 at higher energies (till the next edge is reached).
At x-ray energies, the transitions are mostly from the l and k shells

## Slide 13: Spectral Resolution
With IPCs, the pulse height was a vague indication of photon energy, but it was basically broad-band work (hard or soft) for the first generations of x-ray observatories.
At a throughput price, you can grating disperse x-rays to get good spectral resolution.

## Slide 16: X-ray missions
It was assumed that interstellar gas would limit our view of the x-ray world to very near the Sun.
1949: Gieger counters on V-2 rocket measured x-rays from the Sun
1962: 1st extra-solar X-ray detection, SCO-X1 plus the diffuse x-ray background
1973: Uhuru was the first satellite x-ray mission (400 sources)

## Slide 17
Vela (DOD): x-ray and gamma ray bursts
Then there was a whole slew of satellites.
HEAO-2 (Einstein): 1977, spectral indices and imaging (first satellite with focusing mirrors). (7000 sources)
Now: CHANDRA, XMM, HETE-2
Angular resolution:VELA: 1˚, CHANDRA:1”
Energy Resolution: VELA: 2 , ASCA: 500

## Slide 21: Data Reduction Skills: The Future of Groundbased Astronomy is here!
HEASARC Software Packages
# HEAsoft - A unified release of the FTOOLS and XANADU packages
# FTOOLS - General FITS file utility programs and mission-specific data analysis tools
# XANADU - Suite of spectral (xspec), timing (xronos), and image (ximage) analysis programs
# XSELECT - Multipurpose tool for filtering event files and generating images, spectra, and light curves
# XSTAR - Program for calculating physical conditions and emission spectra in photoionized gases
# fv - Interactive editor and viewer for astronomical data files in FITS format
# Hera - Enables complete interactive analysis over the Internet of data products retrieved from the Browse data archive
# MAKI - A multi-mission observation visualizer and planning utility
# FITSIO - A subroutine library for reading and writing FITS files for C and Fortran programmers
Other Useful Multi-mission Software
# IRAF/PROS - X-ray data analysis package developed and maintained by the ROSAT Science Data Center at CFA
# EXSAS - Extended X-ray Scientific Analysis System for spacial, spectral, and timing analysis. Maintained by a team of the X-ray astronomy group of the MPE at Garching

## Slide 22: Gamma-Ray Astronomy
Explorer X-1, 1961 detected 100 photons
Vela satellites sent up to monitor nuclear weapons testing set the modern stage. Lots of sources away from the Earth, uniformily distributed on the sky
1991, Compton Gamma Ray Observatory was launched.

## Slide 23: Compton GRO
BATSE: Burst and transient, all sky 20-600KeV
OSSE: 0.05-10MeV
COMPTEL: 1-30MeV + 1 degree resolution
EGRET: 20-30MeV and 10 resolution

## Slide 24
BATSE
NaI + PMT
EGRET

## Slide 25
For EGRET spatial and energy resolution, there is layer of spark wire grids behind tantalum foils. Electron-positron pairs produced in the foil and paths tracked through the grids.

## Slide 26: Archive/Data Mining
Papers
  http://adsabs.harvard.edu/abstract_service.html
  http://au.arxiv.org/archive/astro-ph
Catalogues
  http://cdsweb.u-strasbg.fr/CDS.html
Stars
  http://simbad.u-strasbg.fr/
Galaxies
http://nedwww.ipac.caltech.edu/

## Slide 27: Archive/Data Mining
Data
  http://cadcwww.dao.nrc.ca/
    This is an entry to almost everything: Hubble archive, DSS (use ESO version), CFHT archive
  http://www.sdss.org/
  http://arch-http.hq.eso.org/ESO-ECF-Archive.html