## Slide 1: IR Astronomy
Eye response goes to 0 at 7500Å
Silicon bandgap energy of 1.1eV means a hard cutoff in CCD response at 1.1µ
`near-IR’: 1µ - 2.5µ
`mid-IR’: 2.5µ - 25µ
`far-IR’: 25µ - 350µ

## Slide 2: Atmospheric Windows
J H K L M N Q

## Slide 3: Backgrounds
I
108
105
102
1µ 10µ 100µ
2µ
-4 Rayleigh scattered sunlight
273K blackbody
thermal IR
(atmosphere, telescopes)

## Slide 4: Backgrounds

## Slide 5
OH can be resolved
Zodiacal light
atmosphere

## Slide 6
Note vertical scales on plots!

## Slide 9: Why IR?
Galactic dust extinction law:
k2.2µ ~ 0.1k0.5µ
Cool stuff: peak(planck) = 2898/T (µ)
  Cool stars emitted energy peak ~ 1µ
  Giant planets ~ 6-15µ
  Dust re-radiation ~ 20-200µ

## Slide 10: High-z Universe
 = 0(1+z)
@z=1.8 Ca H&K `break’ redshifted to J band
@z=8 L

## Slide 11: Detectors
Original IR detectors were lead-sulfide, then germanium bolometers.
1980’s the first photo-diode (CCD-like) detectors became available with semicondutors that had smaller bandgaps than silicon
Photoconductive: resistance a very sensitive function of T. Ran at liquid helium temperatures (4K).
larger dark currents!

## Slide 12
Material wavelength(µ) Toperate
Si <1.1µ 160K
HgCdTe 0.8 - 5µ 65K
InSb 1 - 5.6µ 35K
SiAs 6 - 27µ 10K

## Slide 13: Special considerations for IR observing
Hardly any!
Chopping (highly variable background)
Backgrounds are enormous
Don’t ignore detector dark/readout noise
Telescope designers be careful
  Baffling
  Cold pupils
  Underfilled secondaries