## Slide 1: Imaging Cameras
Imagers can be put at almost any focus, but most commonly they are put at prime focus or at cassegrain.

## Slide 2
The scale of a focus is given by
S=206265/(D x f#) (arcsec/mm)
Examples:
3m @f/5 (prime) 13.8 arcsec/mm (0.33”/24µpixel)
1m @f/3 (prime) 68.7 arcsec/mm (1.56”/24µpixel)
1m @f/17 (cass) 12.1 arcsec/mm (0.29”/24µpixel)
10m @f/1.5 (prime) 11.5 arcsec/mm (0.27”/24µpixel)
10m @f/15 (cass) 1.15 arcsec/mm (0.03”/24µpixel)
Classical cassegrain (parabolic primary + convex hyperbolic in front of prime focus) has significant coma.

## Slide 3
For a classical cassegrain focus or prime focus with a parabolic primary you need a corrector.
The Richey-Chretien design has a hyperbolic primary and secondary designed to balance out coma and astigmatism in the focal plane.

## Slide 4: Direct Camera design/considerations
LN2 can
Dewar
CCD
dewar window
Preamp
baffles
Shielded cable to controller
shutter
Filter wheel
Field corrector/ADC
Primary mirror

## Slide 5: Shutters
The standard for many years has been multi-leaf iris shutters. As detectors got bigger and bigger, the finite opening time and non-uniform illumination pattern started to cause problems.
2k x 2k 24µ CCD is 2.8 inches along a diagonal.
Typical iris shutter - 50 milliseconds to open. Center of a 1s exposure is exposed 10% longer than the corners.

## Slide 6
Shutter vignetting pattern produced by dividing a 1 second exposure by a 30 second exposure.

## Slide 7: Double-slide system
The solution for mosaic imagers and large-format CCD has been to go to a 35mm camera style double-slide system.

## Slide 8: Filter Wheel
Where do you put the filter? There is a trade off between filter size and how well focused dust and filter imperfections are.

## Slide 9: Drift Scanning
An interesting option for imaging is to park the telescope (or drive it at a non-sidereal rate) and let the sky drift by.
Clock out the CCD at the rate the sky goes by and the accumulating charge ``follows’’ the star image along the CCD.

## Slide 10: Drift Scanning
End up with a long strip image of the sky with a `height’ = the CCD width and a length set by how long you let the drift run (or by how big your disk storage is).
The sky goes by at 15 arcseconds/second at the celestial equator and slower than this by a factor of 1/cos(as you move to the poles.
So, at the equator, PFCam, with 2048 x 0.3” pixels you get an integration time per object of about 40 seconds.

## Slide 11: Drift Scanning
What is the point?
  Superb flat-fielding (measure objects on many pixels and average out QE variations)
  Very efficient (don’t have CCD readout, telescope setting)
Problem:
  Only at the equator do objects move in straight lines, as you move toward the poles, the motion of stars is in an arc centered on the poles.
Sloan digital survey is a good example
Zaritsky Great Circle Camera is another

## Slide 12: Detectors (ESO transition to CCDs)
First astronomical CCD, JPL 400x400

## Slide 13: Pixels/Camera

## Slide 14: Direct Imaging
Filter systems
  Photometry
    Point sources
      Aperture
      PSF fitting
    Extended sources (surface photometry)
    Star-galaxy separation

## Slide 15: Filter Systems
There are a bunch of filter systems
  Broad-band (~1000Å wide)
  Narrow-band (~10Å wide)
  Some were developed to address particular astrophysical problems, some are less sensible.

## Slide 16
3100Å is the UV atmospheric cutoff
1.1µ silicon bandgap

## Slide 17: Filter Choice: Example
Suppose you want to measure the effective temperature of the main-sequence turnoff in a globular cluster.
color relative time to reach Teff=100
B-V 4.2
V-R 11.5
B-I 1.0
B-R 1,7

## Slide 18: Narrow-band Filters
Almost always interference filters and the bandpass is affected by temperature and beam speed:
CWL = 1Å/5˚C
CWL = 17Å; f/13 f/2.8

## Slide 19: Photometry
Aperture Photometry
  DaCosta, 1992, ASP Conf Ser 23
  Stetson, 1987, PASP, 99, 191
  Stetson, 1990, PASP, 102, 932
Sum counts in all pixels in aperture
Determine sky in annulus, subtract off sky/pixel in central aperture

## Slide 20: Aperture Photometry
Total counts in aperture from source
Counts in each pixel in aperture
Number of pixels in aperture
m = c0 - 2.5log(I)

## Slide 21: Aperture Photometry
What do you need?
  Source center
  Sky value
  Aperture radius

## Slide 22: Centers
The usual approach is to use ``marginal sums’’.
: Sum along columns
j
i

## Slide 23: Marginal Sums
With noise and multiple sources you have to decide what is a source and to isolate sources.

## Slide 24
Find peaks: use ∂x/∂x zeros
Isolate peaks: use ``symmetry cleaning’’
  Find peak
  compare pairs of points equidistant from center
  if Ileft >> Iright, set Ileft = Iright
Finding centers: Intensity-weighted centroid

## Slide 25
Alternative for centers: Gaussian fit to 
DAOPHOT FIND algorithm uses marginal sums in subrasters, symmetry cleaning, reraster and Gaussian fit.
Height of peak
Solving for center

## Slide 26: Sky
To determine the sky, typically use a local annulus, evaluate the distribution of counts in pixels in a way to reject the bias toward higher-than-background values.
Remember the 3 Ms.

## Slide 27
Counts
#of pixels
Mode (peak of this histogram)
Arithmetic mean
Median (1/2 above, 1/2 below)
Because essentially all deviations from the sky are positive counts (stars and galaxies), the mode is the best approximation to the sky.

## Slide 28: Some Small Details
Pixels are square. What about the partial pixels at a given radius? Usual approach is to assume uniform brightness throughout pixel and calculate fraction within r of the aperture center.
What about aperture size?

## Slide 29: Aperture size and growth curves
First, it is VERY hard to measure the total light as some light is scattered to very large radius.
Radial intensity distribution for a bright, isolated star.
Radius from center in pixels
Inner/outer sky radii
Perhaps you have most of the light within this radius

## Slide 30
Radial intensity distribution for a faint star:
Same frames as previous example
Bright star aperture
The wings of a faint star are lost to sky noise at a different radius than the wings of a bright star.

## Slide 31: Radial profile with neighbors
Neighbors OK in sky annulus (mode), trouble in star apertures

## Slide 32: One approach is to use `growth curves’
Idea is to use a small aperture (highest S against background and smaller chance of contamination) for everything and determine a correction to larger radii based on several relatively isolates, relatively bright stars in a frame.
Note! This assumes a linear response so that all point sources have the same fraction of light within a given radius.
Howell, 1989, PASP, 101, 616

## Slide 34: Growth Curves
Aperture | 2 | 3 | 4 | 5 | 6 | 7 | 8
Star#1 | 0.43 | 0.31 | 0.17 | 0.09 | 0.05 | 0.02 | 0.00
Star#2 | 0.42 | 0.33 | 0.19 | 0.08 | 0.21 | 0.11 | 0.04
Star#3 | 0.43 | 0.32 | 0.18 | 0.10 | 0.06 | 0.02 | -0.01
Star#4 | 0.44 | 0.33 | 0.18 | 0.22 | 0.14 | 0.12 | 0.14
Star#5 | 0.42 | 0.32 | 0.18 | 0.09 | 0.19 | 0.21 | 0.19
Star#6 | 0.41 | 0.33 | 0.19 | 0.10 | 0.05 | 0.30 | 0.12
cMean | 0.430 | 0.324 | 0.184 | 0.094 | 0.057 | 0.02 | 0.00
∂mag for apertures n-1, n
Sum of these is the total aperture correction to be added to magnitude measured in aperture 1

## Slide 35
Aperture Radius
∂mag[aper(n+1) - aper(n)]
5 10 15 20 25 30
-0.15
-0.10
-0.05
0
0.05

## Slide 36: DAOGROW
Stetson, 1990, PASP, 102, 932 presented a fitting function for growth curves.
Gaussian core + exponential + inverse power law for large radius

## Slide 37: Aperture Photometry Summary
Identify brightness peaks
2.
Use small aperture
3. Add in ``aperture correction’’ determined from bright, isolated stars
Easy, fast, works well except for the case of overlapping images

## Slide 38: Crowded-field Photometry
As was assumed for aperture corrections, all point sources have the same PSF (linear detector).
Various codes have been written that:
  Automatic star finding
  Construction of PSF
  Fitting of PSF to (multiple) stars
DAOPHOT, ROMAPHOT, DOPHOT, STARMAN
Will spend some time on the use of DAOPHOT

## Slide 39: DAOPHOT
Stetson, 1987, PASP, 99, 191
Stetson, DAOPHOT Users’ Manual
Main subroutines:
  FIND
  PHOT
  PSF
  ALLSTAR (DAOPHOT II)
Couple of parameter files:
  daophot.opt
  photo.opt

## Slide 40
daophot.opt
  HI=65635 (in counts)
  LO=5 (in standard deviations: sky-5
  GA=3.9 (gain in e-/dn)
  RE=2.05 (readout noise in units of DN)
  FI=3 (PSF fitting radius)
  PS=12 (PSF radius)
  TH=3.5 (threshold in units of sky standard deviations)
  AN=-6 (analytical form of PSF)
  WA=-2 (`watch’ - level of verbosity for feedback)
  VA=2 (spatial variability of PSF)
photo.opt
  A1=3 (1st aperture radius=3 pixels)
  A2=0 (if a zero is encountered, DAOPHOT ignores the rest of the apertures)
  Etc
  A9=19
  AA=22
  AB=25
  AC=29
  IS=35 (inner sky radius)
  OS=45 (outer sky radius)

## Slide 41: DAOPHOT FIND
Needs gain, RN, HIBAD, LOBAD, FWHM
Find convolves the frame with a gaussian with  FWHM/2.35. This improves the S/N for objects with a point-source PSF.
For subrasters, constructs marginal sums and uses derivative zeros to isolate objects
Fits two 1-D gaussian in x and y
Calculates ``sharpness’’ and ``roundness’’
Writes a .coo file with: n,x,y,mag,sharp,round

## Slide 42
Determine the right threshold with a couple easy tests:
  Plot #stars found vs threshold level
  Use IRAF fields and tvmark to put dots at the x,y positions in the .coo file
Output file default name is framename.coo
First time through a frame, the strong blends will not be properly parsed into individual centroids.

## Slide 43: PHOT
Requires photo.opt file in directory to define apertures and sky annulus
Requires input .coo file
Calculates sky-subtracted magnitude for each aperture (usually only one)
Determines the sky value for each object
Output: framename.ap

## Slide 44: PSF
PSF uses stars on the frame to create a PSF. DAOPHOT uses an analytical core plus a 2-D lookup table.
  For any star: m=c0-2.5log(psf scaling factor)
DAOPHOT options are variants on bivariate:
Fitting radius: ~FWHM; PSF radius: ~ 4 x FWHM

## Slide 45
To construct a PSF
  Choose unsaturated, relatively isolated stars
  If PSF varies over the frame, sample the full field
  Make 1st iteration of the PSF
  Subtract psf-star neighbors
  Make another PSF
Output of PSF routine is a framename.psf which has a header containing the parameters defining the analytical function and an encoded look up table of residuals.

## Slide 46: Allstar (DAOPHOT II)
Use the .ap file and .psf as input (x,y,sky for every object)
Based on PSF radius, group objects into sets that need to be simultaneously fitted with PSFs
Fit PSFs to groups
Return: framename.als
  x, y, mag, ∂mag, chi
Scaling factor ratio of actual psf fit to how well it should have fit

## Slide 48: DAOPHOT run
Attach frame
find (frame.coo)
phot (frame.ap)
PSF loop (frame.psf)
Allstar (frame.als, frames.fits)
Attach subtracted frame
Find (frames.coo)
Phot (frames.ap)
Merge two lists
allstar
Star-subtracted frame

## Slide 49
First find
Second find
galaxy

## Slide 50: Post-DAOPHOT
You usually want to combine photometry in each filter and match up stars in different filters to determine colors.
First, need to determine the coordinate transformation between frames. You can do this and combine photometry or images.
In IRAF, use a list of a matched stars and geotrans and geomap.
There are standalone Stetson programs to combine DAOPHOT-format photometry files

## Slide 51: DAOMATCH
DAOMATCH uses the Method of Matching Triangles. Triangle side length ratios are invariant under rotation, translation, scale change and ``flip’’. Groth, 1986, AJ, 91, 1244. (note: #triangles goes like n!/[3!(n-3)!])
Check bright stars in two files, identify matching triangles, solve for coefficients in:

## Slide 52: DAOMATCH
For dithered frames:
  A,B - x,y offsets
  C,F ~ 1 (scale changes in x and y)
  D,E ~ 0 (cross-terms are non-zero for rotations)
Use this with .als files and produce a .mch file with the coordinate transformations. This is usually used as the first guess, to be fed into DAOMASTER

## Slide 53: DAOMASTER
DAOMASTER takes the DAOMATCH .mch files with transformations and a list of .als files and (1) refines the transformations using all matched stars, (2) derives robust photometric offsets between frames and (3) correctly averages measurements (remember to never average magnitudes!)

## Slide 54: Photometric Calibration
The photometric standard systems have tended to be zero-pointed arbitrarily. Vega is the most widely used and was original defined with V= 0 and all colors = 0.
Hayes & Latham (1975, ApJ, 197, 587) put the Vega scale on an absolute scale.
The AB scale (Oke, 1974, ApJS, 27, 21) is a physical-unit-based scale with:
m(AB) = -2.5log(f) - 48.60
where f is monochromatic flux is in units of erg/sec/cm2/Hz. Objects with constant flux/unit frequency interval have zero color on this scale

## Slide 55: Photometric calibration
Instrumental magnitudes
Counts/sec
minstrumental

## Slide 56: Photometric Calibration
To convert to a standard magnitude you need to observe some standard stars and solve for the constants in an equation like:
Stnd mag
Instr mag
zpt
Extinction coeff (mag/airmass)
airmass
Color term

## Slide 57
Extinction coefficients:
  Increase with decreasing wavelength
  Can vary by 50% over time and by some amount during a night
  Are measured by observing standards at a range of airmass during the night
Slope of this line is c1

## Slide 58
The color terms come about through mismatches between the effective bandpasses of your filter system and those of the standard system. Objects with different spectral shapes have different offsets.

## Slide 59
V=v1+a0
RMS=0.055

## Slide 60
V=vinst+ c0 + c1X
RMS=0.032

## Slide 61
V=vinst+c0+c1X+c2(B-V)
RMS=0.021

## Slide 62: Photometric Standards
Landolt (1992, AJ, 104, 336)
Stetson (2000, PASP, 112, 995)
Fields containing several well measured stars of similar brightness and a big range in color. The blue stars are the hard ones to find and several fields are center on PG sources.
Measure the fields over at least the the airmass range of your program objects and intersperse standard field observations throughout the night.

## Slide 63
Example Landolt Field

## Slide 64: Transfer of the Stnd Transformation
Usually observe standard fields on a night
………………. program fields …………
  Standards measured with growth-curve aperture photometry to estimate the `total’ light
  Program stars measured via frame-dependent PSF scaling factors
For each program field you need to find the magnitude difference between the PSF and `total’ light -- this is called the aperture correction

## Slide 65: Aperture correction procedure
After finding and PSF fitting stars on a frame, subtract the fitted PSFs for all but 20 or 30 relatively isolated objects (after the subtraction, they are hopefully very isolated)
Do growth-curve photometry on the frame and find:
This gets added to all the PSF-based magnitudes on the frame.
Note: check for position-base trends