## Slide 1: AY257: Modern Observational Techniques
This class is mostly about data reduction techniques.
Working through the homework problems is the best way to learn the material
We will work in the IRAF environment. Not necessarily the best, but it is widely available and free.

## Slide 2: Outline
S/N calculations
Planning an observing run
  Proposal Writing
  Aircharts
  Calibration Frames
  Checks during the run
Data Reduction
  Preliminary processing: overscan, bias, flat-fielding
  Photometry
    Imaging cameras
    Point Sources
    Surface Photometry
    Star-galaxy separation
    calibration

## Slide 3: Outline cont.
  Spectral data
    Spectrometer design
    Formats
    Extraction
    Radial velocity measurements
    Equivalent width measurements
    Indices
  IR (to 10µ)
  Radio
  X-ray/gamma-ray astronomy

## Slide 4: Homeworks
Homework should be written up carefully using Latex with embedded figures. Purpose, ``howto’’, results.
Fine to work together, but everyone should do their writeups independently.
Will need access to a computer with IRAF or IDL, Latex or Word, plotting package (e.g. SM) to do the homeworks and writeups.
Learning to use these packages is a great side benefit of the class.

## Slide 5: Bolte Schedule
May 9, 11 out of town

## Slide 6: Digital Detectors
By far the most common detector for wavelengths 300nm<nm is the CCD.

## Slide 7: CCDs
Quantum efficiency is more than an order of magnitude better than photographic plates.
Quantum Efficiency
100%
0%
300nm 500nm 700nm 1000nm
Photographic emulsions
CCD

## Slide 8
These are silicon fab-line devices and complicated to produce.
CCDs remain physically small compared to photographic plates, but they took over rapidly anyway.

## Slide 9
1985 1990 1995 2000 2005
Year
#pixels
107
108
109
1010
2k x 2k

## Slide 10: CCDs: How do they work?
Silicon semiconductors with ``gate’’ structure to produce little potential corrals.
Photons
Electrons bumped into conduction band
Read out and amplify current
A/D convert to DN
`clock’ parallel and serial registers
``CTE’’ > 0.99999
e-
e-
e-
e-
e-

## Slide 11: CCD operation
At room temperature, electrons in high-energy tail of the silicon spontaneously pop up into the conduction band: “dark current”. Cooling the detectors reduced the dark current although at about -120C the quantum efficiency starts to decrease.
Therefore, CCDs usually are put into dewars with liquid nitrogen cold baths and heaters and the temperature is actively controlled to ~1C.
Readout speed is typically adjustable--faster readout gives higher readout noise per pixel.

## Slide 12: CCDs cont.
The potential corrals that define the pixels of the CCD start to flatten as e- collect. This leads first to saturation, then to e- spilling out along columns.
The “inverse gain” is the number of e- per final “count” post the A/D converter.
One very important possibility for CCDs is to tune the response to be linear.

## Slide 13
``Counts’’ = ADU = DN
DN is not the fundamental unit, the # of detected electrons is. The ``Gain’’ is set by the electronics.
Most A/D converters use 16 bits.
DN from: 0 to (216 - 1) = 65535
for unsigned, long integers
Signed integers are dumb: -32735 to +32735
+/-(215 - 1)
Analogue-to-digital unit
DigitalUnit

## Slide 14: What gain do you want?
Example: LRIS-R has a SITe 24µ-pixel CCD with pixel ``wells’’ that hold ~350,000 e-
16-bit unsigned integer A/D saturates at 65525DN
Would efficiently maximize dynamic range by matching these saturation levels:
Note, this undersamples the readout noise and leads to “digitization” noise.

## Slide 15: Signal-to-Noise (S/N)
Signal=R*• t
time
detected e-/second
Consider the case where
we count all the detected
e- in a circular aperture
with radius r.
I
sky
r
r

## Slide 16
Noise Sources:

## Slide 17
S/N for object measured in aperture with radius r: npix=# of pixels in the aperture= πr2
Signal
Noise
All the noise terms added in quadrature
Note: always calculate in e-
Noise from sky e- in aperture
Noise from the dark
current in aperture
Readnoise in aperture

## Slide 18: S/N Calculations
So, what do you do with this?
  Demonstrate feasibility
  Justify observing time requests
  Get your observations right

## Slide 19: Side Issue: S/N mag
m
m
Note:in log +/- not symmetric
This is the basis of people referring to +/- 0.02mag error as “2%”
Fractional error

## Slide 20: S/N mag
S/N mag
2 0.44
10 0.10
100 0.01

## Slide 21: How do you get values for some of these parameters?
Dark Current: CCD@-120˚C < 2e-/pix/hour
Insb: ~2e-/pix/sec
RN: CCD: 2 - 6 e-/pix
Insb: 10 - 25 e-/pix
R*: for a given source brightness, this can be calculated for any telescope and total system efficiency.
In practice: Go to the facility WWW site for everything!

## Slide 22: Source Count Rates
Example: LRIS on Keck 1
for a B=V=R=I=20mag object @ airmass=1
B | 1470 e-/sec
V | 1521 e-/sec
R | 1890 e-/sec
I | 1367 e-/sec
To calculate R* for a source of arbitrary brightness only requires this table and a bit of magnitude math.

## Slide 23: Source Count Rates
Let I2 be the intensity for the fiducial m=20 object

## Slide 24: Rsky
Signal from the sky background is present in every pixel of the aperture. Because each instrument generally has a different pixel scale, the sky brightness is usually tabulated for a site in units of mag/arcsecond2.
˝
(mag/
)
Lunar age (days) | U | B | V | R | I
0 | 22.0 | 22.7 | 21.8 | 20.9 | 19.9
3 | 21.5 | 22.4 | 21.7 | 20.8 | 19.9
7 | 19.9 | 21.6 | 21.4 | 20.6 | 19.7
10 | 18.5 | 20.7 | 20.7 | 20.3 | 19.5
14 | 17.0 | 19.5 | 20.0 | 19.9 | 19.2
NaD
OH
Hg

## Slide 26
S/N - some limiting cases. Let’s assume CCD with Dark=0, well sampled read noise.
Bright Sources:
(R*t)1/2 dominates noise term
Sky Limited
Note: seeing comes in with npix term

## Slide 27: What is ignored in this S/N eqn?
Bias level/structure correction
Flat-fielding errors
Charge Transfer Efficiency (CTE) 0.99999/pixel transfer
Non-linearity when approaching full well
Scale changes in focal plane
A zillion other potential problems

## Slide 28: Writing Proposals
First and foremost: Scientific Justification!
  Give context
  Clearly state what unanswered questions are to be addressed
  Clearly state what you will do new or better
Look Competent and Smart
  Do S/N and exposure time calculations
  Defend choice of filters/spectral resolution sample size etc.

## Slide 29: Observing
Rule #1 -- keep collecting photons!
Know your S/N targets
Plan the night out carefully ahead of time
Useful tools:
  Aircharts

## Slide 30
Right Ascension (RA) and Declination (Dec) are equatorial sky coordinates
Like longitude and latitude (respectively) on the surface of the Earth but fixed on the sky
Aligned with the Earth’s axis so the RA and Dec for celestial objects changes as the Earth’s orbit precesses. Need to specify the “epoch” of the coordinates.

## Slide 31: Hour angles and airmass
The sidereal time gives the right ascension that is passing through the meridian. My index point is 12h is overhead at local midnight on March 21. Sky advances 2 hours per month.
The hour angle is the time before or after a particular RA is at the meridian. HA=LST-RA
Airmass is a combination of the HA and the difference between the telescope latitude and the pointing declination. Airmass~sec(zenith angle)

## Slide 32
IRAF Airchart in the mtools packages is very handy.
Typically observe with airmass=X<2
Atmospheric dispersion can be a problem for X>1.5
http://www.eso.org/observing/bin/skycalcw/airmass

## Slide 33
There are often other limits that govern where you can point in the sky.
East
North
1h
2h
3h
Dec=-30

## Slide 34: Decisions before observing
Sometimes, the gain in e-/DN for the system
On-chip binning?
  Smaller files (not important)
  Faster readout time (can be important)
  Less readout noise per area detector (can be important)
For direct imaging in broadband filters, readnoise is very rarely an issue. You want to have the FWHM of point sources to be at least 2.5 pixels to properly sample the PSF. If you are oversampled, that doesn’t usually have any dire consequences. The readout time can be a deciding factor.

## Slide 35: Binning for spectra
.
Sometimes, RN is a significant component of the noise. Having fewer pixels under the spectrum reduces the noise in a resolution element.
Binning in Spectral direction can reduce resolution
Spatial direction
Binning in the spatial direction can compromise fitting the sky lines

## Slide 36: Observing Checklist: Afternoon
Bias frames - should be boring! WWW site for instrument should have an example to compare to.
  Move filterwheels, gratings, telescope, dome during readout to see if it will be safe to do so during the night
Dome Flats
  Is the shutter opening?
  Shutter timing observations
For spectra, check the grating tilts for proper wavelength range
Things are working- take flats, arcs, biases, darks
Get quick-look reduction procedures in place

## Slide 37: At Night
Efficiency is everything!
  Have the shutter open
  Know your S/N goals
  Have targets queued up
  Check focus
  Have the shutter open
Be looking at your data in near real time including flat-fielding and bias subtraction

## Slide 38: Telescope Focus
Whether you focus yourself or the telescope operator does it for you, you need to always be checking radial profiles.
Plot intensity values for pixels that intersect circles

## Slide 39
Using the ``r’’ command in IRAF’s imexam, you can produce radial profiles for any object in a frame. :.snap eps in the graphics window will output an .eps file.
Poor focus (scatter is lack of roundness and probably astigmatism)
Excellent focus. Very round (and dangerously sharp) image

## Slide 40
Well focussed star
Saturated star
Galaxy

## Slide 41
Way out of focus (donut).

## Slide 42: Focus frames
Set focus, start exposure.
Pause exposure, move telescope, change focus
Repeat
Make a double telescope move on the last focus value, then read out

## Slide 43: Splitting Exposures
How long to expose? Once in the sky-limited regime, the S/N only depends on the total exposure time. There is only the CCD readout time penalty to be paid by splitting long exposures into multiple shorter exposure.
Why do shorter exposures?
  Cosmic ray rejection
  Increase dynamic range
  ``in-field dithering’’ along slit or on the sky can help with flat fielding
  Reduce risk

## Slide 44: Preliminary Processing
There are two types of instrumental signature to remove:
  Additive:
    Bias Level
    Bias Structure
    Dark Counts
    ``charge skimming’’
  Multiplicative:
    Q.E. variations on all scales
Constant # of counts added independent of the brightness of the source(s).
Constant fractional effect

## Slide 45: Bias Correction
Bias level and any y (along columns) gradient is taken out via overscan subtraction.
Bias structure is taken out by subtracting a zero-level frame.
In IRAF ccdproc takes care of both.

## Slide 46: Overscan
After reading out the CCD `real’ pixels, you can continue to read out virtual pixels and record the bias level and read noise of the amplifiers. These virtual pixels are called the overscan region
Active area of CCD
Row or line #
Column #
overscan region

## Slide 47: Two amplifier overscan

## Slide 49: Overscan subtraction
First you need to identify the relevant columns.
In IRAF use the format:
[x1,x2:y1,y2]
Sky level
Overscan#1
Oscan#2
In IRAF, plots like this are made using implot

## Slide 50: Colbias
The overscan subtraction is accomplished by fitting a smooth function to the average of several columns in the overscan region.
The value of the fitted curve is subtracted from each row. This accounts for a mean bias level and any gradient in along columns.

## Slide 51
Smooth fit is subtracted from each row
Average several

## Slide 52: Flat Fielding
There are pixel-to-pixel QE variations and lower spatial frequency QE variations in all electronic detectors. The goal of flat-fielding is to multiply every pixel by the correct normalizing factor to eliminate these QE differences.
Ideally, illuminate the detector with a source that is as flat on the sky as the background and collect at least a million e- per pixel. Then could flat-field to =0.1%.

## Slide 53: Flat Fielding
If you could illuminate the CCD uniformly, then normalize the mean to 1, this image could be divided into every frame.
For direct imaging, usually use a combination of:
  Dome Flats
  Twilight Flats
  Dark Sky Flats

## Slide 54: Dome Flats
Put some quartz (hot, continuum source) lamps on the telescope and illuminate a white screen or spot on the dome.
These often don’t work very well for two reasons:
  The lamps are always too cool (red)
  The dome is not even close to infinity and usually illuminates the primary differently than the sky
But, you can collect a lot of photons during the day

## Slide 55: Twilight Flats
These often work pretty well
The Sun is pretty hot, the scattering surface illuminates the telescope just like the dark night sky
Doesn’t use dark time

## Slide 56: Dark-sky Flats
These tend to work very well. They match the sky perfectly
They sometimes require useful dark time
They sometimes contain fringes

## Slide 57: Stars and Galaxies
For twilight and dark sky flats you have a problem in that they contain stars and galaxies. The usual trick is to move the telescope between exposures and then do a non-registered stack of the frames in each filter.
Median or better yet minmax rejection (for example, in the frame combining can effectively eliminate all the stars and galaxies in the combined flat.

## Slide 58: Minmax rejection
Pixel value: 1000 200 180 180
Average with minmax rejection, reject 2 highest value averaging lowest two will give the sky value. NOTE! Must normalize frames to common mean or mode before combining! Sometimes it is necessary to pre-clean the frames before combining.

## Slide 59: Combining Frames
In IRAF, imcombine is the task to combine frames.
  combine=average
  reject=minmax
  scale=mode
  nlow=0
  nhigh=2

## Slide 60: Flat fielding tricks
Combine domes (high counts, bad illumination) with dark sky flats (low counts, excellent illumination).
  Spatially smooth (or fit low-order surface to) both combined dome and combined dark sky. > sDome, sDark
  Remove dome low-spatial-frequency pattern: Dome/sDome
  sDark is the sky flat with the low-f pattern already removed.
  Best of both worlds is (Dome/sDome) x sDark

## Slide 61
PFCam flat fields
I-band
V-band
U-band
Dust on filter
Rings due to non uniform thinning
Note differences with color. This means that objects with different spectra will be flat-fielded slightly incorrectly.
Two amplifer readout

## Slide 63: Flat-field tests
Take cuts through your flat-fielded frames and make sure the sky is flat (check corners). IRAF implot
In blank areas, make sure the pixel-to-pixel variations are consistent with shot noise from the sky level. IRAF imexam and the `m’ key.