## Slide 1: Spectra
Bowen, 1962, Astronomical Techniques, pg 34.
Pogge, 1992, ASP Conf. Ser.#23, pg.160

## Slide 4: Dispersing Elements
Most common is probably the reflecting diffraction grating.
Grating equation: m = d[sin() + sin(ß)]

ß
order groove spacing
d

## Slide 5: Grating dispersion
Think of the Young Double-slit experiment with many slits very closely spaced together (100 - 10,000+ lines/mm) and for non-monochromatic light - same constructive/destructive interference phenomenon from path-length differences.
Note: ruling gratings is not easy! Spacing tolerance is ~1nm. Richardson has a machine in a room kept a constant temperature to 0.01˚C

## Slide 6
Differentiate the grating equation wrt outgoing angle and get the angular dispersion
The linear dispersion is:
Å/mm  d/m
lines/mm
order
in camera focal plane

## Slide 7: Spectrometers
Gratings require collimated (parallel beam) light so the basic long-slit spectrometer:
collimator
grating
camera
detector
telescope focal
plane
Can often change the grating tilt to vary the wavelengths arriving on the detector

## Slide 8: Transmission gratings
There are also different versions of transmission gratings.
  Transmission grating
  Grisms - add a prism for zero-deviation transmission dispersion
  Volume Phase Holographic Gratings: VPH - use modulations of the index of refraction rather than surface structures to produce dispersion. High efficiency.

## Slide 9: Long-slit Spectra Geometry
In the camera focal plane there is the dispersion direction perpendicular to the slit and the spatial direction along the slit.

## Slide 10
seeing disk
Length set by decker
in telescope focal plane

## Slide 11: Spectral Resolution
R=/
For slit spectral, depends on slit width and grating choice.
Examples:
  V filter: 5500Å/1000Å=5.5
  LRIS-R: 1˝ ~4 pixels FWHM
    150 l/mm grating: R~6500/20 ~325
    600 l/mm grating: R~6500/5 ~1300
    1200 l/mm grating: R~6500/2.6 ~2600

## Slide 12: LRIS (Keck Obs WWW page)
Grating
Name Grooves Blaze Wave Dispersion Spectral coverage
(l/mm) (Å) (Å/pix) (Å/2048 pix)
150/7500 150 7500 4.8 9830
300/5000 300 5000 2.55 5220
400/8500 400 8500 1.86 3810
600/5000 600 5000 1.28 2620
600/7500 600 7500 1.28 2620
600/10000 600 10000 1.28 2620
831/8200 831 8200 0.93 1900
900/5500 900 5500 0.85 1740
1200/7500 1200 7500 0.64 1310

## Slide 13: Orders and blocking filters
400nm 200nm 133.3nm
For order n, at n there is also order m light with wavelength m=(n/m)n
m=1 m=2 m=3
800nm 400nm 266.6nm

## Slide 14
For higher orders with <310nm it’s not an issue as the atmosphere cuts out all the light (can still be an issue for calibration sources).
But, if you are working in the red (>640nm) in 1st order, you need to block the 2nd order light.
If you are working in a higher order, may need to block red light from lower orders.

## Slide 15
KPNO 2.1m Goldcam blue blocking filters

## Slide 16: Grating Efficiencies

## Slide 18: Dichroics and Double Spectrometers
Telescope focal plane
dichroic
Reflection gratings
grisms

## Slide 19: Spectrometer Throughput
Spectrometer throughput ranges from a few percent to ~50%. The losses accumulate fast. Dispersing elements are usually a big hit, then the losses at multiple surfaces go like (transmission)n where n is the number of surfaces in the collimator and camera elements (n can be pretty big)
0.988*0.7*0.8=0.47
Camera/coll grating ccd
with 8 surfaces

## Slide 20
Another throughput issue: slit losses can be very significant!

## Slide 21: Spectrometer Observing Considerations
On-chip binning:
night-sky line
stellar spectrum
spectral direction
spatial direction
I
line#
You are going to sum over these lines in the extraction anyway. On-chip binning will reduce RN x #pixels
For LRIS-B, 0.15 arcsec/pixel in the spatial direction

## Slide 22
In the spectral direction, binning can reduce spectral resolution. If the FWHM of arclamp lines ≥ 5 pixels, you can start to think about binning. Lots of time you are interested in accurate line centers and higher moments of the spectral line profiles in which case, well sampled features are a good idea.

## Slide 23: S/N for Spectral Observations
On-chip binning:
night-sky line
stellar spectrum
spectral direction
spatial direction
I
line#

## Slide 24: S/N for Spectral Observations
Often sum counts again in the spectral direction to determine S/Nresolution element.
Note! Assumes sky noise is at the shot noise limit. Imperfectly modeled and subtracted sky lines are worse than this.
For spectra the S/N usually varies considerably with wavelength:
  Absorption, emission, continuum
  Sky lines
  System efficiency with wavelength

## Slide 25: More Spectral Considerations
Differential Atmospheric Dispersion (Filippenko, 1982, PASP, 94 715)
Dispersion in the atmosphere causes chromatic distortion of images that gets larger at blue wavelengths at fixed airmass and larger with airmass at fixed central wavelength.
@X=1.5, 1.3 separation between 350nm and 550nm
index of refraction
zenith distance

## Slide 26
Two problems:
1) Preferentially lose red (or blue) light out of the slit.
2) If guiding on a particular wavelength of light, the object at other wavelengths will move out of the slit.
X=1 X=1.5

## Slide 27
Two solutions:
  Align slit along the parallactic angle

## Slide 28: Build an ADC

## Slide 29: Uncorrected

## Slide 30: Corrected with ADC

## Slide 31: Linear ADC
LADC displaces focus:
Must repoint telescope
Tilted focal surface -- must refocus telescope for prism separation and rotator angle
Possible changes in vignetting
Displaced pupil at grating (barely OK)
Must oversize/displace prisms to minimize clear aperture

## Slide 33
KPNO 4m rotating `Risley’ prisms.
Central guider wavelength
Factor of 3+

## Slide 34: Multiobject Spectroscopy
Very popular option for the last decade or so.
  Multislit
  Fiber-fed
  Fabry-Perot
  IFU

## Slide 35
Remember the simple case: carefully rotated long slit. Note: better have an ADC.
Telescope focal plane
Night sky lines
Spectral direction
Spatial direction
Spectrometer camera focal plane

## Slide 36: Multislit spectroscopy

## Slide 40
Night sky line
boxes
1 slit
object spectrum

## Slide 42
Advantages of multislits:
  High throughput
  Can choose slit width and length
  Good sky subtraction
  Can place slits close together in telescope focal plane
Disadvantages of multislits:
  wavelength coverage varies with the slit position
  do not always use the detector area efficiently.

## Slide 43: Fiber-fed MOS
ASP Conf Series #37, 1997
Examples:
  Lick 3m MOS (80 fibers/1º field)
  HYDRA@ WIYN (200+ fibers/1º field)
  2DF@ AAT (400 fibers/2º field)

## Slide 44: 2DF focal plane

## Slide 45: 2DF buttons+fibers

## Slide 46
spectrometer
pseudoslit
Spectra on CCD

## Slide 47
Advantages of multi-fiber systems
  Large fields
  Uniform wavelength coverage
  Efficient use of detector area
Disadvantages
  Minimum separation is between a few and 10+ arcseconds
  Fiber losses are significant and grow with time (fiber are delicate)
  Sky subtraction difficulties
  Setup times can be long

## Slide 48
Add in `button’ losses and focal-ratio degredation.
Fiber loss is per unit length

## Slide 49: IFUs

## Slide 50: Echelle Spectrometers
If after grating dispersion you `cross disperse’ the spatially coincident orders you can separate the orders in the camera focal plane.
This is an echelle spectrometer. Usually do the initial dispersion with a fine ruled grating and the cross dispersiing with a prism.
Local examples are the Lick Hamilton Spectrometer and Keck HIRES

## Slide 51
Order# wavelength

## Slide 53: Fabry-Perot
A final type of spectrometer is a F-P system

## Slide 54
F-P data cube
Color-coded velocity map