## Slide 1: Spectral Reduction Procedures
There are good introductions/cookbooks available from the IRAF folks. The introduction to spectral reductions is at the class WWW site.
There are many ways to accomplish most tasks. Will run through a basic approach to reducing long slit spectra.

## Slide 2
Steps:
  Bias and overscan correction
  Flat-fielding
    Note: need to remove large-scale variations in the spectral dimension
  Identify location of the spectrum
  Identify location of sky samples
  Extract spectrum
    Trace
    Collapse lines
    Interpolate sky and subtract
  Use stellar aperture to extract arc spectrum
    Note: sometimes do the flat-fielding here
  Fit pixel-wavelength map and apply to spectrum
  Derive flux calibration and apply to spectrum

## Slide 3
Star+sky
Quartz lamp flat
HgCdNe line lamps

## Slide 4: Note about Observing
If spectrometer is not flexure compensated, the usual procedure is to obtain a line lamp spectrum (or two) and flat-field spectrum (or two) at the position of your program object. Sometimes even bracket the program exposures with arcs and flats.
Depending on program, observe:
  Flux standard
  Radial velocity standard
  Hot rapid rotator to identify terrestrial atmospheric absorption
If no ADC, pay attention to position angle!

## Slide 5
Packages in noao.twodspec.apextract
  Need to set the dispersion axis
tw>epar apextract
PACKAGE = twodspec
TASK = apextract
(dispaxi= 1) Dispersion axis (1=along lines, 2=along columns)
(databas= database) Database
(verbose= no) Verbose output?
(logfile= ) Text log file
(plotfil= ) Plot file
(version= APEXTRACT V3.0: August 1990)
(mode = ql)
($nargs = 0)
Dispersion axis

## Slide 6
noao.twod.apextract
tw> apex
apall apedit apflatten apnormalize apscatter
apdefault@ apfind apmask aprecenter apsum
apdemos. apfit apnoise apresize aptrace
apall combines parameter files for all the rest of the tasks
Dispersion axis along lines (`1’ to IRAF)

## Slide 7
PACKAGE = apextract
TASK = apall
input = List of input images
(output = ) List of output spectra
(apertur= ) Apertures
(format = multispec) Extracted spectra format
(referen= ) List of aperture reference images
(profile= ) List of aperture profile images
(interac= yes) Run task interactively?
(find = yes) Find apertures?
(recente= yes) Recenter apertures?
(resize = yes) Resize apertures?
(edit = yes) Edit apertures?
(trace = yes) Trace apertures?
(fittrac= yes) Fit the traced points interactively?
(extract= yes) Extract spectra?
(extras = yes) Extract sky, sigma, etc.?
(review = yes) Review extractions?
Multispec: star, sky, S/N
Useful for arcs/faint spectra/discontinuous spectra
Usually “no”
keep spectrum, sky and S/N in 3-d output fits file

## Slide 8
(line = INDEF) Dispersion line
(nsum = 10) Number of dispersion lines to sum or median
# DEFAULT APERTURE PARAMETERS
(lower = -5.) Lower aperture limit relative to center
(upper = 5.) Upper aperture limit relative to center
(apidtab= ) Aperture ID table (optional)
# DEFAULT BACKGROUND PARAMETERS
(b_funct= chebyshev) Background function
(b_order= 1) Background function order
(b_sampl= -10:-6,6:10) Background sample regions
(b_naver= -3) Background average or median
(b_niter= 0) Background rejection iterations
(b_low_r= 3.) Background lower rejection sigma
(b_high_= 3.) Background upper rejection sigma
(b_grow = 0.) Background rejection growing radius
Default is center

## Slide 9
# APERTURE CENTERING PARAMETERS
# AUTOMATIC FINDING AND ORDERING PARAMETERS
# RECENTERING PARAMETERS
# RESIZING PARAMETERS
# TRACING PARAMETERS
(t_nsum = 10) Number of dispersion lines to sum
(t_step = 10) Tracing step
(t_nlost= 3) Number of consecutive times profile is lost befo
(t_funct= legendre) Trace fitting function
(t_order= 2) Trace fitting function order
(t_sampl= *) Trace sample regions
(t_naver= 1) Trace average or median
(t_niter= 0) Trace rejection iterations
(t_low_r= 3.) Trace lower rejection sigma
(t_high_= 3.) Trace upper rejection sigma
(t_grow = 0.) Trace rejection growing radius
Skipping the details of these for now
Trace finds the `y’ position of the peak as a function of x position

## Slide 10
(backgro= fit) Background to subtract
(skybox = 1) Box car smoothing length for sky
(weights= none) Extraction weights (none|variance)
(pfit = fit1d) Profile fitting type (fit1d|fit2d)
(clean = yes) Detect and replace bad pixels?
(saturat= 31000.) Saturation level
(readnoi= 0.) Read out noise sigma (photons)
(gain = 1.) Photon gain (photons/data number)
(lsigma = 4.) Lower rejection threshold
(usigma = 4.) Upper rejection threshold
(nsubaps= 1) Number of subapertures per aperture
(none,average,median,min,fit)

## Slide 11: Example Extraction
cl>apall b188 output=b188.ms
Find apertures for b188? (yes):
Number of apertures to be found automatically (1):
Edit apertures for b188? (yes):
Aperture #1
Sky apertures
Commonly used options:
? -- help
l -- set lower ap limit
u -- set upper ap limit
b -- to tweak sky aperture
w -- window the plot
? -- window help
e -- expand plot
q -- happy, continue

## Slide 12
`b’ option:
Fitted sky value
Commonly-used commands:
z -- deletes nearest aperture
s -- define new aperture
f -- redo fit
:order n -- set order of fit
q -- accept fit and go to previous panel

## Slide 13
Trace:
column
column
line
line
order 2 fit
:o 7
f
order 7 fit

## Slide 14
Splot:
cl>splot b188.ms
aperture
band (spec,sky,S/N)
Extracted spectrum in pixel space
Common splot options:
? -- lists all the options
%-- select new band
m-- gives statistics
e-- eq. width, line centers
s-- smooth
t-- fit continuum
w--window plot

## Slide 15: Sky

## Slide 16: Band #4: S/N

## Slide 17: Line Lamps
Use a pre-defined aperture, trace for extracting arcs. Lines are often tilted or curved.
cl>apall arc output=arc.ms ref=b188 find- trace- background=none

## Slide 18
Sometimes fit a master arc taken in the afternoon and use arcs taken adjacent to program objects to make a zeropoint shift to the wavelength solution.

## Slide 19: Flat-fields
Can flat-field original frames in 2-D format, but more commonly, the flat-field image is extracted with the same aperture as the program object.
In the spirit of flat-fielding for direct images, you would like a source that is uniform in the spatial direction AND has a flat spectrum. In practice, all flat-field lamps (usually a hot quartz lamp) have a strong spectral (continuum) signature.
So, usually extract flat, then fit a function in the spectral direction and divide this out to leave the pixel-to-pixel response.

## Slide 20
Blue Red
Quartz lamp

## Slide 21
Can do any of the following:
Divide by extracted flat and normalized later
Fit extracted flat and normalize, then divide
Use twod.longslit.response and approximate the aperture (returns normalized, extracted flat response from 2-D spectrum

## Slide 22: Wavelength Calibration
Identify the lines in your lamp-line spectrum
Fit line centers, derive function to map pixel scale to wavelength scale
Associate arc+solution with program spectra
Apply the `dispersion’ solution, usually writing a short version of the solution to the header

## Slide 23: Example, from Lick KAST WWW pages

## Slide 24
IRAF wavelength fitting routine:
  noao.oned.identify
PACKAGE = onedspec
TASK = identify
images = Images containing features to be identified
(section= middle line) Section to apply to two dimensional images
(databas= database) Database in which to record feature data
(coordli= linelists$idhenear.dat) User coordinate list (typically user uses their own list)
(units = ) Coordinate units
(nsum = 10) Number of lines/columns/bands to sum in 2D image
(match = -3.) Coordinate list matching limit
(maxfeat= 50) Maximum number of features for automatic identif
(zwidth = 100.) Zoom graph width in user units
(ftype = emission) Feature type
(fwidth = 4.) Feature width in pixels
(cradius= 5.) Centering radius in pixels
(thresho= 0.) Feature threshold for centering
(minsep = 2.) Minimum pixel separation
(functio= spline3) Coordinate function
(order = 1) Order of coordinate function
(sample = *) Coordinate sample regions

## Slide 25
First identify window
Commonly-used commands:
? -- help
m -- mark a line
c -- center next feature
l -- locate the rest of the lines
d -- delete a line
f -- fit (brings up new window)
w -- window

## Slide 28
:label both

## Slide 29: Applying wavelength solution
PACKAGE = onedspec
TASK = refspectra
input = extracted_spectrum List of input spectra
(referen= arc) List of reference spectra
(apertur= ) Input aperture selection list
(refaps = ) Reference aperture selection list
(ignorea= yes) Ignore input and reference apertures?
(select = interp) Selection method for reference spectra
(sort = jd) Sort key
(group = ljd) Group key
(time = no) Is sort key a time?
(timewra= 17.) Time wrap point for time sorting
(overrid= no) Override previous assignments?
(confirm= yes) Confirm reference spectrum assignments?
(assign = yes) Assign the reference spectra to the input spectr
(logfile= STDOUT,logfile) List of logfiles
(verbose= no) Verbose log output?
answer = Accept assignment?
(mode = ql)
Sophisticated auto assignment options

## Slide 30
PACKAGE = onedspec
TASK = dispcor
input = List of input spectra
output = List of output spectra
(lineari= yes) Linearize (interpolate) spectra?
(databas= database) Dispersion solution database
(table = ) Wavelength table for apertures
(w1 = INDEF) Starting wavelength
(w2 = INDEF) Ending wavelength
(dw = INDEF) Wavelength interval per pixel
(nw = INDEF) Number of output pixels
(log = no) Logarithmic wavelength scale?
(flux = yes) Conserve flux?
(samedis= no) Same dispersion in all apertures?
(global = no) Apply global defaults?
(ignorea= no) Ignore apertures?
(confirm= no) Confirm dispersion coordinates?
(listonl= no) List the dispersion coordinates only?
(verbose= yes) Print linear dispersion assignments?
Last step: apply dispersion solution. In IRAF, done in header
cl>dispcor b188.ms w188.ms
b188.ms: REFSPEC1 = 'arc.ms 1.'
w188.ms: ap = 1, w1 = 3312.038, w2 = 5494.508, dw = 1.820242, nw = 1200

## Slide 32
Inner 200 pixels

## Slide 33
r > 200 pixels

## Slide 34: Flexure
Two lamp spectra from LRIS taken at different telescope positions
Note the shift is (1) significant and (2) constant along the dispersion
reidentify allows a quick/automatic refitting of arcs taken during the night. Can also use single arc solution from afternoon calibrations and apply a zeropoint (wavelength) shift for each program spectrum based on night sky line positions

## Slide 35: Short reidentify aside
Can reidentify the line lamp spectrum at a range of line values (in a single spectrum)
Use fitcoords to take the fit as a function of line number plus transform to remap the 2D image to be rectilinear in dispersion-spatial.
Useful for long-slit work with resolved objects.

## Slide 36: Flux Calibration
There are lists of spectrophotometric standard stars:
  Oke, J. B. 1990, AJ, 99, 1621
  Stone, R. P. S. 1996, ApJS, 107, 423
  Massey, P., & Gronwall, C. 1990, ApJ, 358, 344
  IRAF: onedstds$
  Usual zeropoint is based on Vega:
  F5556Å=3.52 x 10-20 erg/cm2/s/Hz (V=0.048 mag)
  Note: In IRAF, you can specify the broadband magnitude of each
  star to do a rough zeropoint correction for slit losses.

## Slide 37
noao.oned
  standard: identifies standard stars by name, associates an extinction curve, gets airmass exposure time. Output is a file (default name std)
  sensfunc: given extinction function, tabulated standard system flux and your observed spectrum calculate a sensitivity function.
  calibrate: applies the sensitivity function to spectra

## Slide 38
standard interactive graphic
Sometimes exclude lines as the result is resolution dependent

## Slide 39
sensfunc interative graphic

## Slide 40
Raw extracted Spectrum
Flux calibrated

## Slide 41: Echelle format spectra
In apall, each
order will be
an aperture.
Each will have
to be traced.
Often the
background
apertures need
to be set for
each order
individually

## Slide 42
Seeing disk
Slit length
Inter-order

## Slide 43
ESI spectra
Inner order regions

## Slide 44
Inner order flux ≠ 0

## Slide 45
For most echellegrams, need to take an extra step of removing scattered light. The idea is to fit a 2-d surface to the inner-order light and subtract this surface before aperture extraction.
noao.echelle has a task apscatter to do this.
Need to identify and trace orders to identify the inner-order regions
Scattered light fit

## Slide 46: Analysis procedures: Equivalent Width Measurements
noao.oned task splot is a powerful measuring tool.
Often start by normalizing a spectrum. In splot, the ‘t’ option allows you to interactively do this
z- delete region
s- define region
:o n - switch fit to order n
f- refit
q- exit normalizing task

## Slide 47: splot help
? - This display r - Redraw the current window
/ - Cycle thru short help on stat line s - Smooth (boxcar)
a - Autoexpand between cursors t - Fit continuum(*)
b - Toggle base plot level to 0.0 u - Adjust coordinate scale(*)
c - Clear and redraw full spectrum v - Velocity scale (toggle)
d - Deblend lines using profile mode w - Window the graph
e - Equiv. width, integ flux, center x - Connects 2 cursor positions
f - Arithmetic functions: log, sqrt... y - Plot std star flux from calib file
g - Get new image and plot z - Expand x range by factor of 2
h - Equivalent widths(*) ) - Go to next spectrum in image
i - Write current image as new ima ( - Go to previous spectrum in image
j - Fudge a point to Y-cursor value # - Select new line/aperture
k - Profile fit to single line(*) % - Select new band
l - Convert to F-lambda $ - Toggle wavelength/pixel scale
m - Mean, RMS, snr in marked region - - Subtract deblended fit
n - Convert to F-nu , - Down slide spectrum
o - Toggle overplot of following plot . - Up slide spectrum
p - Convert to wavelength scale I - Interrupt task immediately
q - Quit and exit <space> - Cursor position and flux

## Slide 48
‘e’
Center:4857.537 eqw: 26.0823

## Slide 49
(*) For 'h' key: Measure equivalent widths
a - Left side for width at 1/2 flux l - Left side for continuum = 1
b - Right side for width at 1/2 flux r - Right side for continuum = 1
c - Both sides for width at 1/2 flux k - Both sides for continuum = 1
(*) For 'k' key: Second key may be used to select profile type
g - Gaussian, l - Lorentzian, v - Voigt, all others - Gaussiank
Other splot eqw options:

## Slide 50
Center: 4857.31 eqw:29.49 lfwhm: 47.45
‘k’ + ‘l’

## Slide 51
‘k’+’g’
Center: 4857.38 eqw: 23.38 gfwhm:41.44

## Slide 52: rvcorrect
Galactic center
In noao.rv is rvcorrect
Based on date and time of the observation and the RA and DEC of the object it will return and write keywords into the header with the heliocentric correction to back out the motions of the Earth around the Sun and the Earth around its axis (the diurnal velocity), motion of the Earth around the Earth-moon barycenter and the Sun’s peculiar motion wrt circular velocity at the mean distance from the Galactic center (LSR). You want the components of these motions in the direction of the object.
The help for this task has all the formulae required to make the calculations

## Slide 53
Usually need to set the keyword translation file to fit the headers of your particular frames using keywpars.
rvcorrect:
rv> rvcorrect
# RVCORRECT: Observatory parameters for Lick Observatory
# latitude = 37:20.6
# longitude = 121:38.2
# altitude = 1290
## HJD VOBS VHELIO VLSR VDIURNAL VLUNAR VANNUAL VSOLAR
2452727.89086 0.00 -8.25 -2.18 -0.107 0.003 -8.143 6.070
Julian date heliocentric correction correction to LSR
Earth’s spin Earth’s orbit
Earth-moon motion

## Slide 54: Radial velocity measurements
Method 1 is to measure line centroids usually after making a zeropoint correction based on measuring a few night sky lines (in splot you can use the “u” and “z” keystroke command to accomplish this).
Get line centers with “e” or one of the line fitting options, calculate doppler shift, apply the heliocentric correction.

## Slide 55: Cross-correlation:FXCOR
Tonry & Davis, 1979, A.J. 84, 1511.
noao.rv fxcor is a pretty good implementation.
Need a template spectrum and an object spectrum.
First, continuum is fitted and subtracted, then any filtering that is to be applied is applied, then a cross-correlation carried out, peak identified and fit.

## Slide 56
Continuum fit object and template spectra
s: set sample
x: do correlation
o: fit object cont.

## Slide 57
Correlation peak and fit
Bad filtering/cont fit

## Slide 59
Radial velocity precision/accuracy
R=2500 (LRIS/KAST): 120km/s
Centroid to 1/20 resolution element gives a precision of 5 km/s (ignoring wavelength calibration uncertainties).
HIRES@R=50000 and 1/20th: 0.3 km/sec

## Slide 60
For most spectrometers, systematic errors dominate by ~2km/sec. Flexure, illumination differences between sky and lamp paths, asymmetric line profiles due to detector and spectrometer optics shortcomings, spectrometer focal-plane scale shifts due to refocus/temperature changes, etc.
Sun reflex motion due to Jupiter is 0.0124km/sec - planet searching is a new ballgame. At this level you even need to worry about the barycentric corrections: 1 m/sec corresponds to determining the mid-time of an observation to 30 seconds.

## Slide 61
Solutions for really high precision work are to environment control stationary spectrometers (coude or Nasmyth platform) and to use a stable, in-spectrum wavelength calibration source.
Campbell & Walker (1979, PASP, 91, 540) proposed hydrogen-fluoride in a cell in front of the spectrometer slit to superpose narrow lines at zero velocity on the spectrum. Showed 15 m/sec precision was possible. HF was described as “obnoxious”

## Slide 62
Butler, et al. 1996, PASP, 108, 500: 3m/s
Marcy, & Butler, 1992, PASP, 104, 270