## Slide 1: Lecture 13 The applications of tomography: MCAO, MOAO, GLAO
Claire Max
AY 289
February 20, 2020

## Slide 2: Outline of lecture
What is AO tomography?
Applications of AO tomography
  Laser tomography AO (LTAO)
  Multi-conjugate AO (MCAO)
  Multi-object AO (MOAO)
  Ground-layer AO (GLAO)
Much of this lecture is based on presentations by Don Gavel, Lisa Poyneer, Francois Rigaut, and Olivier Guyon. Thanks!

## Slide 3: Limitations for AO systems with one guide star
3
Isoplanatic Angle
  Limits the corrected field
θ0
h
r0
Notes: 3

## Slide 4: Limitations for AO systems with one guide star
4
Cone effect
Notes: 4

## Slide 5: Limitations for AO systems with one guide star
5
Cone effect
  Missing turbulence outside and above cone
  Spherical wave “stretching” of wavefront
More severe for larger telescope diameters
h
r0
Notes: 5

## Slide 6
Fundamental problem to solve: Isoplanatic Angle
If we assume perfect on-axis correction,
and a single turbulent layer at altitude h,
the variance (sq. radian) is :
σ2 = 1.03 (θ/θ0)5/3
Θ = angle to optical axis,
θ0 = isoplanatic angle:
θ0 = 0.31 (r0/<h>)
D = 8 m, r0 = 0.8 m,
<h> = 5 km => θ0 = 10”
h

## Slide 7: Francois Rigaut’s diagrams of tomography for AO
90 km
“Missing” Data
Credit: Rigaut, MCAO for Dummies

## Slide 8: What is Tomography ? 2. Wider field of view, no cone effect
90 km
Credit: Rigaut, MCAO for Dummies
Tomography lets you reconstruct turbulence in the entire cylinder of air above the telescope mirror

## Slide 9: Concept of a metapupil
Can be made larger than “real” telescope pupil
Increased field of view due to overlap of fields toward multiple guide stars

## Slide 10: How tomography works: from Don Gavel
10
Each wavefront sensor measures the integral of index variation along the ray lines
The line integral along z determines the kz=0 Fourier spatial frequency component
Projections at several angles sample the kx,ky,kz volume
kX
kZ
Fourier slice theorem in tomography
(Kak, Computer Aided Tomography, 1988)
Fourier Transform
x - z plane
kx - kz plane
Notes: 10

## Slide 11: How tomography works: from Don Gavel
11
kX
kZ
Fourier Transform
x - z plane
kx - kz plane
The larger the telescope’s primary mirror, the wider the range of angles accessible for measurement
In Fourier space, this means that the “bow-tie” becomes wider
More information about the full volume of turbulence above the telescope
Notes: 11

## Slide 12: How tomography works: some math
y
Assume we measure y with our wavefront sensors
Want to solve for x = value of δ(OPD)
The equations are underdetermined – there are more unknown voxel values than measured phases ⇒ blind modes. Need a few natural guide stars to determine these.
where
  y = vector of all WFS measurements
  x = value of δ(OPD) at each voxel in turbulent volume above telescope
x
  A is a forward propagator
Notes: 12

## Slide 13: Solve for the full turbulence above the telescope using the back-propagator
y
x
y
x
  AT is a back propagator along rays back toward the guidestars
  y = vector of all WFS measurements
  x = value of δ(OPD) at each voxel in turbulent volume above telescope
  Use iterative algorithms to converge on the solution.
Notes: 13

## Slide 14: LGS Related Problems: “Null modes”
Five “Null Modes” are not seen by LGS (Tilt indetermination problem)
Need 3 well spread tip-tilt stars to control these modes
Tilt Anisoplanatism : Low order modes produce Tip-Tilt at altitude
  → Dynamic Plate Scale changes
Credit: Rigaut, MCAO for Dummies

## Slide 15: Outline of lecture
Review of AO tomography concepts
AO applications of tomography
  Laser tomography AO (LTAO)
  Multi-conjugate AO (MCAO)
  Multi-object AO (MOAO)
  Ground-layer AO (GLAO)

## Slide 16: Laser Tomography AO: High-Order Correction; Fixes Cone Effect
Narrow field, cone effect fixed
one DM
Corrected field: 10’s of arc sec

## Slide 17: Multi-Conjugate AO: Wider Field Correction
Corrects over wider field, at a penalty in peak Strehl
≥ 2 DMs
Corrected field: up to ~2 arc min

## Slide 18: Multi-Object AO: Wider Field but only correct objects you are interested in
Correct over narrow field of view located anywhere w/in wide field of regard
One DM for each object of interest
Multiple Narrow Field DMs
Corrected field: N x 10’s of arc sec

## Slide 19: Ground Layer AO: Widest field, only modest AO correction
Quite modest correction over a much wider field of view
One DM conjugate to ground
Corrected field: 5 -10 arc min

## Slide 20: Corrected fields of view vary depending on method
Method |  | Corrected field of view
Laser Tomography AO | LTAO | 10’s of arc sec
Multi-Object AO | MOAO | N x 10’s of arc sec
Multi-Conjugate AO | MCAO | ≤ about 2 arc min
Ground Layer AO | GLAO | A few to 10 arc min

## Slide 21: Outline of lecture
Review of AO tomography concepts
AO applications of tomography
  Multi-conjugate adaptive optics (MCAO)
  Multi-object adaptive optics (MOAO)
  Ground-layer AO (GLAO)

## Slide 22: What is multiconjugate AO?
Deformable mirror
Turbulence Layers
Credit: Rigaut, MCAO for Dummies

## Slide 23: What is multiconjugate AO?
Deformable mirrors
Turbulence Layers
Credit: Rigaut, MCAO for Dummies

## Slide 24: Difference between Laser Tomography AO and MCAO
Laser Tomography AO can be done with only 1 deformable mirror
If used with multiple laser guide stars, reduces cone effect
MCAO uses multiple DMs, increases field of view

## Slide 25: “Star Oriented” MCAO
WFSs
Guide Stars
DM2
Telescope
High Altitude Layer
Ground Layer
DM1
WFC
Each WFS looks at one star
Global Reconstruction
n GS, n WFS, m DMs
1 Real Time Controller
The correction applied at each DM is computed using all the input data.
Credit: N. Devaney

## Slide 26: MCAO Simulations, 3 guide stars
3 guide stars, FoV = 1.5 arc min
3 guide stars, FoV = 1 arc min
Credit: N. Devaney
Optimum guide star separation: about one isoplanatic angle
Strehl at 2.2 μm

## Slide 27: First operational MCAO system: GEMS at Gemini South 8m telescope

## Slide 28: GEMS image of star formation in Orion

## Slide 29
Orion star forming region:
Compare GEMS MCAO with ALTAIR single conjugate AO on Gemini North Telescope
ALTAIR GEMS

## Slide 30: GEMS MCAO: very good uniformity across 87” x 87” field
Credit: Rigaut et al. 2013

## Slide 31: Outline of lecture
Review of AO tomography concepts
AO applications of tomography
  Multi-conjugate adaptive optics (MCAO)
  Multi-object adaptive optics (MOAO)
  Ground-layer AO (GLAO)

## Slide 32: Distinctions between multi-conjugate and multi-object AO
DMs conjugate to different altitudes in the atmosphere
Guide star light is corrected by DMs before its wavefront is measured
Only one DM per object, conjugate to ground
Guide star light doesn’t bounce off small MEMS DMs in multi-object spectrograph
?
1-2 arc min
Closed-Loop
Open-Loop

## Slide 33: Multi-Object AO
Correct over multiple narrow fields of view located anywhere w/in wide field of regard
In most versions, each spectrograph or imager has its own MEMS AO mirror, which laser guide star lights doesn’t bounce off of
Hence this scheme is called “open loop”: DM doesn’t correct laser guide star wavefronts before LGS light goes to wavefront sensors
In one version, each LGS also has its own MEMS correction

## Slide 34: Science with MOAO: multiple deployable spatially resolved spectrographs
A MEMS DM underneath each high-redshift galaxy, feeding a narrow-field spatially resolved spectrograph (IFU)
No need to do AO correction on the blank spaces between the galaxies

## Slide 35: Why does MOAO work if there is only one deformable mirror in the science path?
Tomography lets you measure the turbulence throughout the volume above the telescope
90 km

## Slide 36: Why does MOAO work if there is only one deformable mirror in the science path?
Tomography lets you measure the turbulence throughout the volume above the telescope
In the direction to each galaxy, you can then project out the turbulence you need to cancel out for that galaxy
90 km

## Slide 37: MOAO Demonstration Systems
CANARY (Durham, Obs. de Paris, ONERA, ESO)
  MOAO pathfinder for E-ELT
  On William Herschel Telescope
  First NGS, then Rayleigh guide stars
RAVEN (U Victoria, Subaru, INO, Canadian NRC)
  MOAO demonstrator for Subaru telescope
  3 NGS wavefront sensors
  Field of regard > 2.7 arc min

## Slide 39: Both E-ELT and TMT have done early designs for MOAO systems
Artist’s sketch of EAGLE MOAO system for E-ELT
One of the constraints is that the spectrographs are very large!
Hard (and expensive) to fit in a lot of them

## Slide 40: Outline of lecture
Review of AO tomography concepts
AO applications of tomography
  Multi-conjugate adaptive optics (MCAO)
  Multi-object adaptive optics (MOAO)
  Ground-layer AO (GLAO)

## Slide 41: Ground layer AO: do tomography, but only use 1 DM (conjugate to ground layer)
Credit: J-M Conan
GLAO uses 1 ground-conjugated DM, corrects near-ground turbulence
Or instead of tomography, can just average over the guide stars

## Slide 42: Correcting just the ground layer gives a very large isoplanatic angle
Strehl = 0.38 at θ = θ0
θ0 is isoplanatic angle
θ0 is weighted by high-altitude turbulence (z5/3)
If turbulence is only at low altitude, overlap is very high.
If you only correct the low altitude turbulence, the isoplanatic angle will be large (but the correction will be only modest)
Telescope
Common
Path

## Slide 43
Credit: A. Tokovinin
time

## Slide 44: Several observatories have ambitious GLAO projects today
Early pathfinders: SOAR (4.25m), William Herschel Telescope (4.2m), MMT (6.5m)
Recently on VLT (8m), LBT (2x8m)
Longer term on Giant Magellan Telescope, E-ELT
Why is it worth the large investment “just” to decrease “seeing” disk by factor of 1.5 to 2 ?
  Large spectrographs can take advantage of smaller image (smaller slit)
  Potential improved SNR for background-limited point sources
  Less variability in PSF

## Slide 45: GLAO on the MMT Telescope
Michael Hart et al. , 5 Rayleigh laser guide stars
FWHM decreased from 0.85 arc sec to 0.28 arc sec (!)

## Slide 46: GLAO on the MMT Telescope
Michael Hart et al. , 5 Rayleigh laser guide stars

## Slide 48: `Imaka: GLAO on UH 88” Telescope
Natural guide star constellation
GLAO reduces two things:
FWHM
Variability of FWHM

## Slide 49: ‘Imaka GLAO reduces PSF variability
GLAO
No GLAO

## Slide 50: Summary
Tomography: a way to measure the full volume of turbulence above the telescope
Once you have measured the turbulence there are several ways to do the wavefront correction
  Laser Tomography AO: Multiple laser guide stars, 1 DM, corrects cone effect. Narrow field.
  Multi-conjugate AO: Multiple DMs, each optically conjugate to a different layer in atmosphere. Wider field of view.
  Multi-object AO: Correct many individual objects, each over a small field. Each has very good correction. Wider field of regard.
  Ground-layer AO: Correct just ground layer turbulence. Very large field of view but only modest correction.
All four methods will be used in the future

## Slide 51: Corrected fields of view vary depending on method
Method |  | Corrected field of view
Laser Tomography AO | LTAO | 10’s of arc sec
Multi-Object AO | MOAO | N x 10’s of arc sec
Multi-Conjugate AO | MCAO | ≤ about 2 arc min
Ground Layer AO | GLAO | A few to 10 arc min