## Slide 1: Lecture 14 Extreme Adaptive Optics
Claire Max
AY 289
February 26, 2020
Based in part on slides from Bruce Macintosh and Sandrine Thomas

## Slide 2: Outline
Science parameter space for Exoplanet systems
Direct imaging of exoplanets with ground-based AO
Approaches to high-contrast imaging with current telescopes: Angular Differential Imaging
Coronagraphs to block light from host star
Gemini Planet Imager: one example of the current state of the art
Recent scientific results: directly imaged planets and disks

## Slide 3: Exoplanets as of 2020
Today 30-40 directly imaged exoplanets

## Slide 4: Working requirements for direct imaging
Contrast between flux from host star and planet
  Depends on wavelength, type of planet, type of star, distance of planet from star, etc.
Order of magnitude for sun-like star
  Earth: visible 10-9 to 10-10
  mid-IR 10-7
  Required contrast ratios for gas giants and for M dwarf host starts are not so stringent (10-6 ?)
Inner Working Angle typically a few 𝜆 / D

## Slide 6: Brightness of ExAO targets: Gas Giants
Marley et al 2007
Hot start
Low-entropy core accretion models
HR8799
ExAO regime
Normal AO regime

## Slide 7: First images of an extrasolar planetary system (Keck and Gemini AO)
Marois et al. 2008 Science Mag

## Slide 8: More directly imaged exoplanets
Beta Pic b
VLT NACO
51 Eri b
GPI
PDS 70
SPHERE

## Slide 9: Conventional AO limited by scattered light
Strehl ratio S
Halo intensity 1-S

## Slide 10
“Extreme” AO (ExAO)
gain > S/(1-S)

## Slide 11: But – this assumes no non-common path errors and no AO artifacts

## Slide 12: Keck AO Image of a bright star

## Slide 13: Inner part of image - artifacts due to AO optics

## Slide 14
Image 1
Image 2 (+ 5 minutes)
Subtraction
Angular Differential Imaging
Marois et al 2006

## Slide 15
+
=

## Slide 16: Image processing to suppress light from host star
Marois et al.

## Slide 17: From Olivier Guyon’s Annual Reviews paper

## Slide 18: Coronagraphs
Invented by Bernard Lyot in 1930 for studying the corona of the sun without waiting for an eclipse
Block the sun’s light with a circular mask in the focal plane
Problem: diffraction from the sharp edges of the mask

## Slide 19: Cartoon of Lyot Coronagraph
Credit: Subaru website

## Slide 20: How can we control diffraction?
PSF=|FT(A)|2
A
PSF

## Slide 21: Lyot coronagraph (Lyot, 1933)
Starlight

## Slide 22: Lyot coronagraph (Lyot, 1933)
Planet
Sivaramakrishnan et al 2001 has a nice 1-d analysis of how this works

## Slide 23: Large variety of coronagraph ideas
Lyot family:
  Basic: Lyot 1939 MNRAS 99, 538; Sivaramakrishnan et al 2001
  Band-limited: Kuchner & Traub 2003
  Apodized: Soummer 2005 Ap.J. 618, L161
Apodizers:
  Shaped-pupil: Kasdin et al 2003, Kasdin et al 2005 Applied Optics 44 1177, etc.
  Phase-induced apodizer: Guyon et al 2005 Ap.J. 622, 744
Interference / wave-optics
  4-quadrant phase mask: Rouan et al 2000 PASP 777 1479
  Nulling interferometer/coronagraphs: Mennesson et al. 2004 Proc. SPIE 4860, 32
Optical Vortex Coronagraphs
Most practical coronagraphs only work at > 3-5 λ/D
Control of phase errors is as important as controlling diffraction

## Slide 24: Coronagraph also improves stability
From Olivier Guyon Annual Reviews paper

## Slide 25: Shaped-pupil coronagraphs to make dark holes (Kasdin et al. 2003)
Pupil
PSF

## Slide 26
AO Timelag
WFS measurement
Inner working distance ~ 3-5 λ/D
Fitting error
Outer working distance ~ N λ/D

## Slide 27: Random intensity of all the Fourier components produces speckles

## Slide 28: As speckles average out (t ~ D/vwind) planets can be detected

## Slide 29: Must get rid of static errors as well

## Slide 30: ExAO 0 nm static errors, 5 MJ/500 MYr planet, 15 minute integration

## Slide 31: ExAO 1 nm static errors, 5 MJ/500 MYr planet, 15 minute integration

## Slide 32: ExAO 2 nm static errors, 5 MJ/500 MYr planet, 15 minute integration

## Slide 33: ExAO 5 nm static errors, 5 MJ/500 MYr planet, 15 minute integration

## Slide 34: Evolution of AO Systems
Milli et al. 2017

## Slide 35: Extreme AO Systems today
From Olivier Guyon Annual Reviews paper

## Slide 36: Schematic of Gemini Planet Imager

## Slide 37: Comparison of original Keck AO and GPI AO parameters
 | Keck AO (1999) | GPI (2010)
Deformable mirror | 349 actuators (240 active) | 4096 actuators (1809 active)
Subaperture | 56 cm | 18 cm
Control rate | 670 Hz | 2000 Hz
Wavefront sensor | Shack-Hartmann 400 – 1000 nm | Spatially-filtered Shack-Hartmann 700-900 nm
Strehl @ 1.65 mm | 40% | > 90%
Guide star mag (NGS only) | R < 13.5 mag. | I < 9 mag. ( V < 11)

## Slide 38: Data pipeline assembles cubes: image of planet as function of wavelength
Christian Marois, HIA

## Slide 39: For Class Projects, how to calculate contrast ratio?
Not a simple expression, as it depends on removing internal wavefront errors as well as atmospheric ones, coronagraph performance, etc
One very rough guess (from Milli et al. 2017):
In real systems this is an under-estimate of the contrast
For ExAO, want very high Strehl (>90%)

## Slide 40: References, part 1
Angel, R, “Ground based imaging of extrasolar planets using adaptive optics’, 1994 Nature 368, 203 (Original exoplanet paper)
Burrows, A., et al., “A nongray theory of extrasolar planets and brown dwarfs”, 1997 Ap.J 491, 856 (Planet models)
Sivaramakrishnan, A., et al., “Ground-based coronagraphy with High-Order Adaptive optics”, 2001 Ap.J. 552, 397 (Lyot coronagraphs)
Kasdin, N.J., et al, 2003, “Extrasolar planet finding via optimized apodized pupil and shaped pupil coronagraphs”, Ap.J. 582, 1147
Kuchner, M, and Traub, W., “A Coronagraph with a Band-limited Mask for Finding Terrestrial Planets” 2002 Ap.J. 570, 200 (improved Lyot coronagraph)
Sivaramakrishnan, A., et al, “Speckle decorrelation and dynamic range in speckle noise limited imaging”, 2002 Ap.J. 581, L59 (2nd-order PSF expansion)
Perrin, M., et al. “The structure of the High Strehl Ratio Point-Spread Functions”, 2003, Ap.J. 596, 702 (high-order PSF expansion)
Poyneer, L, and Macintosh, B., “Spatially-filtered wavefront sensor for high-order adaptive optics”, 2004, JOSA A 21, 810 (aliasing + WFS)
Guyon, O., et al. “Theoretical Limits on Extrasolar Terrestrial Planet Detection with Coronagraphs”, 2006 Ap.J.S. 167, 81

## Slide 41: References, part 2
LaFreniere, D., et al., “A new algorithm for point-spread function subtraction for high-contrast imaging”
Macintosh, B., et al, “The Gemini Planet Imager: From Science to Design to Construction”, 2008 Proc. SPIE 7015-18
Marois, C., et al., 2000, “Efficient Speckle Noise Attenuation in Faint Companion Imaging”, 2000 Proc. SPIE 767, 91
Marois, C., et al., 2006, “Angular Differential Imaging: A Powerful High-Contrast Technique”, 2006 Ap.J. 6541, 556
Marois, C., Macintosh, B., Barman, T., et al, “Direct Imaging of Multiple Planets Orbiting the Star HR8799”, 2008 Science 5906, 1348
Poyneer, L., Macintosh, B., and Veran, J-P., “Fourier transform wavefront control with adaptive prediction of the atmosphere”, 2007 JOSA A 24, 2645