## Slide 1: Atmospheric Turbulence Lecture 2, ASTR 289
Claire Max
UC Santa Cruz
January 14, 2020

## Slide 2: Observing through Earth’s Atmosphere
"If the Theory of making Telescopes could at length be fully brought into Practice, yet there would be certain Bounds beyond which telescopes could not perform …
For the Air through which we look upon the Stars, is in perpetual Tremor ...
The only Remedy is a most serene and quiet Air, such as may perhaps be found on the tops of the highest Mountains above the grosser Clouds."
Isaac Newton

## Slide 3: Newton was right!
Summit of Mauna Kea, Hawaii (14,000 ft)

## Slide 4: Outline of lecture
Physics of turbulence in the Earth’s atmosphere
  Location
  Origin
  Energy sources
Mathematical description of turbulence

## Slide 5: Atmospheric Turbulence: Main Points
The dominant locations for index of refraction fluctuations that affect astronomers are the atmospheric boundary layer and the tropopause (we will define these)
Atmospheric turbulence (mostly) obeys “Kolmogorov statistics”
Kolmogorov turbulence is derived from dimensional analysis (heat flux in = heat flux in turbulence)
Structure functions (we will define these!) derived from Kolmogorov turbulence are
All else will follow from these points!

## Slide 6: Atmospheric Turbulence: Topics
What determines the index of refraction in air?
Origins of turbulence in Earth’s atmosphere
Energy sources for turbulence
Kolmogorov turbulence models

## Slide 7: Index of refraction of air
Refractivity of air
  where P = pressure in millibars, T = temp. in K, λ in microns
  n = index of refraction.
Key points:
  Index of refraction is very close to unity
  Wavelength dependence of index of refraction is very weak!
    Less than 1% effect at wavelengths ~ 1 micron

## Slide 8: Fluctuations in index of refraction are due to temperature fluctuations
Temperature fluctuations  index fluctuations
Take derivative of expression on previous slide
  (pressure is constant, because velocities are highly sub-sonic -- pressure differences are rapidly smoothed out by sound wave propagation)

## Slide 9: Turbulence arises in many places (part 1)
stratosphere
Heat sources w/in dome
boundary layer
~ 1 km
tropopause
10-12 km
wind flow around dome

## Slide 10: Two examples of measured atmospheric turbulence profiles
Credit: cute-SCIDAR group, J. J. Fuensalida, PI

## Slide 11: Turbulence within dome: “mirror seeing”
When a mirror is warmer than dome air, convective equilibrium is reached.
Remedies: Cool mirror itself, or blow air over it.
To control mirror temperature: dome air conditioning (day), blow air on back (night), send electric current through front Al surface-layer to equalize temperature between front and back of mirror
credit: M. Sarazin
credit: M. Sarazin
convective cells are bad

## Slide 12: Natural flushing by wind can frequently reduce “mirror seeing”
Credit: Majewski, Univ. of Virginia

## Slide 13: Modern observatory domes have louvres to let wind flow through
Gemini dome
VLT Domes

## Slide 14: Turbulence also arises from wind flowing over the telescope dome
“Wake Turbulence” – you may not want to point telescope in direction opposite to wind, on windy night
Computational fluid dynamics simulation (D. de Young)

## Slide 15: Turbulent boundary layer has largest effect on “seeing”
Wind speed must be zero at ground, must equal vwind several hundred meters up (in the “free” atmosphere)
Adjustment takes place at bottom of boundary layer
  Where atmosphere feels strong influence of surface
  Turbulent viscosity slows wind speed to zero
Quite different between day and night
  Daytime: boundary layer is thick (up to a km), dominated by convective plumes rising from hot ground. Quite turbulent.
  Night-time: boundary layer collapses to a few hundred meters, is stably stratified. See a few “gravity waves.” Perturbed if winds are high.

## Slide 16: Convection takes place when temperature gradient is steep
Daytime: ground is warmed by sun, air is cooler
If temp. gradient between ground and ~ 1 km is steeper than “adiabatic gradient,” warm volume of air raised upwards will have cooler surroundings, will keep rising
These warm volumes of air carry thermal energy upwards
UCAR large eddy simulation of convective boundary layer

## Slide 17: Boundary layer is much thinner at night: Day ~ 1 km, Night ~ few hundred meters
Surface layer: where viscosity is largest effect
Daytime convection
Couldn’t find source for this figure

## Slide 18: Implications: solar astronomers vs. night-time astronomers
Daytime: Solar astronomers have to work with thick and messy turbulent boundary layer
Night-time: Less total turbulence, but still the single largest contribution to “seeing”
Neutral times: near dawn and dusk
  Smallest temperature difference between ground and air, so wind shear causes smaller temperature fluctuations

## Slide 19: Concept Question
Think of as many reasons as you can why high mountain tops have the best “seeing” (lowest turbulence). Prioritize your hypotheses from most likely to least likely.
Use analogous reasoning to explain why the high Atacama Desert in Chile also has excellent “seeing”.
Mauna Kea, Hawaii
Atacama Desert, Chile

## Slide 20: Turbulence in the “free atmosphere” above the boundary layer
Strong wind shear at tropopause

## Slide 21: Wind shear mixes layers with different temperatures
Wind shear  Kelvin Helmholtz instability
If two regions have different temperatures, temperature fluctuations δT will result
T fluctuations ⟹ index of refraction fluctuations
Computer simulation by Ceniceros and Roma, UCSB

## Slide 22: Sometimes clouds show great Kelvin-Helmholtz vortex patterns
A clear sign of wind shear

## Slide 23: Leonardo da Vinci’s view of turbulence

## Slide 24: Kolmogorov turbulence in a nutshell
Big whorls have little whorls,
Which feed on their velocity;
Little whorls have smaller whorls,
And so on unto viscosity.
L. F. Richardson (1881-1953)

## Slide 25: Kolmogorov turbulence, cartoon
Outer scale L0
ground
Inner scale l0
hν
convection
solar
hν
Wind shear

## Slide 26: Kolmogorov turbulence, in words
Assume energy is added to system at largest scales - “outer scale” L0
Then energy cascades from larger to smaller scales (turbulent eddies “break down” into smaller and smaller structures).
Size scales where this takes place: “Inertial range”.
Finally, eddy size becomes so small that it is subject to dissipation from viscosity. “Inner scale” l0
L0 ranges from 10’s to 100’s of meters; l0 is a few mm

## Slide 27: Breakup of Kelvin-Helmholtz vortex
Start with large coherent vortex structure, as is formed in K-H instability
Watch it develop smaller and smaller substructure
Analogous to Kolmogorov cascade from large eddies to small ones
http://www.youtube.com/watch?v=hUXVHJoXMmU

## Slide 28: How large is the Outer Scale?
Dedicated instrument, the Generalized Seeing Monitor (GSM), built by Dept. of Astrophysics, Nice Univ.)

## Slide 29: Median Outer Scale ~ 25-30 m, from Generalized Seeing Monitor measurements at Calern, Fr
Aristidi et al. 2019

## Slide 30: Concept Question
What do you think really determines the outer scale in the boundary layer? At the tropopause?
Hints:

## Slide 31: The Kolmogorov turbulence model, derived from dimensional analysis (1)
v = velocity, ε = energy dissipation rate per unit mass, = viscosity, l0 = inner scale, l = local spatial scale
Energy/mass = v2/2 ~ v2
Energy dissipation rate per unit mass
  ε ~ v2/τ = v2 / (l / v) = v3 / l
  v ~ (ε l )1/3
  Energy v2 ~ ε 2/3 l 2/3

## Slide 32: Kolmogorov Turbulence Model (2)
1-D power spectrum of velocity fluctuations: k = 2π / l
Φ(k) Δk ~ v2 ~ ( ε l )2/3 ~ ε 2/3 k -2/3 or, dividing by k,
  Φ(k) ~ k -5/3 (one dimension)
3-D power spectrum: Φ3D(k) ~ Φ / k 2
  Φ3D(k) ~ k -11/3 (3 dimensions)
For a more rigorous calculation: V. I. Tatarski, 1961, “Wave Propagation in a Turbulent Medium”, McGraw-Hill, NY

## Slide 33: Lab experiments agree
k (cm-1)
Power (arbitrary units)
Air jet, 10 cm diameter (Champagne, 1978)
Assumptions: turbulence is homogeneous, isotropic, stationary in time
Slope -5/3
L0
l0

## Slide 34: The size of the inertial range is related to the Reynolds number
Outer scale of turbulence: L0
  Size of the largest turbulent eddy
Inner scale of turbulence: l0
  Below this scale, collisional viscosity wipes out any remaining velocity gradients
Can show that
“Fully developed turbulence”: Re > 5 x 103 (or more)

## Slide 35: What does a Kolmogorov distribution of phase look like?
Position (meters)
Position (meters)
A Kolmogorov “phase screen” courtesy of Don Gavel
Shading (black to white) represents phase differences of ~1.5 μm
r0 = 0.4 meter

## Slide 36: Structure functions are used a lot in AO discussions. What are they?
Mean values of meteorological variables change over minutes to hours. Examples: T, p, humidity
If f(t) is a non-stationary random variable,
  Ft(τ) = f ( t +τ) - f ( t) is a difference function that is stationary for small τ .
Structure function is measure of intensity of fluctuations of f (t) over a time scale less than or equal to τ :
  Df(τ) = < [ Ft(τ) ]2> = < [ f (t + τ) - f ( t) ]2 >

## Slide 37: More about the structure function (1)

## Slide 38: Structure function for atmospheric fluctuations, Kolmogorov turbulence
Scaling law we derived earlier: v2 ~ ε2/3 l2/3 ~ r 2/3 where r is spatial separation between two points
Heuristic derivation: Velocity structure function ~ v2
Here Cv2 = constant to clean up “look” of the equation

## Slide 39: Derivation of Dv from dimensional analysis (1)
If turbulence is homogenous, isotropic, stationary
  where f is a dimensionless function of a dimensionless argument.
Dimensions of α are v2, dimensions of β are length, and they must depend only on ε and ν (the only free parameters in the problem).
  [ ν ] ~ cm2 s-1 [ ε ] ~ erg s-1 gm-1 ~ cm2 s-3

## Slide 40: Derivation of Dv from dimensional analysis (2)
The only combinations of ε and ν with the right dimensions are

## Slide 41: What about temperature and index of refraction fluctuations?
Temperature fluctuations are carried around passively by velocity field (incompressible fluids).
So T and N have structure functions similar to v:
DT ( r ) = < [ T (x ) - T ( x + r ) ]2 > = CT2 r 2/3
DN ( r ) = < [ N (x ) - N ( x + r ) ]2 > = CN2 r 2/3

## Slide 42: How do you measure index of refraction fluctuations in situ?
Refractivity
Index fluctuations
So measure δT , p, and T; calculate CN2

## Slide 43: Simplest way to measure CN2 is to use fast-response thermometers
DT ( r ) = < [ T (x ) - v ( T + r ) ]2 > = CT2 r 2/3
Example: mount fast-response temperature probes at different locations along a bar:
X X X X X X
Form spatial correlations of each time-series T(t)

## Slide 44: Assumptions of Kolmogorov turbulence theory
Medium is incompressible
External energy is input on largest scales (only), dissipated on smallest scales (only)
  Smooth cascade
Valid only in inertial range l << L0
Turbulence is
  Homogeneous
  Isotropic
In practice, Kolmogorov model works surprisingly well!
Questionable

## Slide 45: Typical values of CN2
Index of refraction structure function
DN ( r ) = < [ N (x ) - N ( x + r ) ]2 > = CN2 r 2/3
Night-time boundary layer: CN2 ~ 10-13 - 10-15 m-2/3
10-14
Paranal, Chile, VLT

## Slide 46: Turbulence profiles from SCIDAR
Eight minute time period (C. Dainty, NUI)
Siding Spring, Australia
Starfire Optical Range, Albuquerque NM

## Slide 47: Atmospheric Turbulence: Main Points
Dominant locations for index of refraction fluctuations: atmospheric boundary layer and tropopause
Atmospheric turbulence (mostly) obeys Kolmogorov statistics
Kolmogorov turbulence is derived from dimensional analysis (heat flux in = heat flux in turbulence)
Structure functions derived from Kolmogorov turbulence:
All else will follow from these points!

## Slide 49: Part 2: Effect of turbulence on spatial coherence function of light
We will use structure functions D ~ r2/3 to calculate various statistical properties of light propagation thru index of refraction variations

## Slide 50: Definitions - Structure Function and Correlation Function
Structure function: Mean square difference
Covariance function: Spatial correlation of a function with itself

## Slide 51: Relation between structure function and covariance function
A problem on future homework:
  Derive this relationship
  Hint: expand the product in the definition of Dϕ ( r ) and assume homogeneity to take the averages
Structure function
Covariance function

## Slide 52: Definitions - Spatial Coherence Function
Spatial coherence function of field is defined as
        Covariance for complex fn’s
    Note that Hardy calls this function but I’ve called it CΨ (r) in order to avoid confusion with the correlation function Bϕ ( r ) . CΨ (r) is a measure of how “related” the field Ψ is at one position (e.g. x) to its values at neighboring positions (say x + r ).

## Slide 53: Now evaluate spatial coherence function CΨ (r)
For a Gaussian random variable with zero mean, it can be shown that
So
So finding spatial coherence function CΨ (r) amounts to evaluating the structure function for phase Dϕ ( r ) !

## Slide 54: Solve for Dϕ( r ) in terms of the turbulence strength CN2 (1)
We want to evaluate
Recall that
So next we need to know the phase covariance:

## Slide 55: Solve for Dϕ( r ) in terms of the turbulence strength CN2 (2)
But for a wave propagating vertically (in z direction) from height h to height h + δh.
Here n(x, z) is the index of refraction.
Hence

## Slide 56: Solve for Dϕ( r ) in terms of the turbulence strength CN2 (3)
Change variables:
Then

## Slide 57: Solve for Dϕ( r ) in terms of the turbulence strength CN2 (4)
Now we can evaluate phase structure function Dφ( r )

## Slide 58: Solve for Dϕ( r ) in terms of the turbulence strength CN2 (5)
But

## Slide 59: Finally we can evaluate the spatial coherence function CΨ (r) (!)
For a slant path you can add factor ( sec θ )5/3 to account for dependence on zenith angle θ
Concept Question: Note the scaling of the coherence function with separation, wavelength, turbulence strength. Think of a physical reason for each.

## Slide 60: Given the spatial coherence function, calculate effect on telescope resolution
Outline of derivation:
Define optical transfer functions of telescope, atmosphere
Define r0 as the telescope diameter where the two optical transfer functions are equal
  OTFtelescope = OTFatmosphere
Calculate expression for r0

## Slide 61: Define optical transfer function (OTF)
Imaging in the presence of imperfect optics (or aberrations in atmosphere): in intensity units
Image = Object Point Spread Function
Take Fourier Transform:
Optical Transfer Function = Fourier Transform of PSF
convolved with

## Slide 62: Examples of PSF’s and their Optical Transfer Functions
Seeing limited PSF
Diffraction limited PSF
Intensity
θ
θ
Intensity
Seeing limited OTF
Diffraction limited OTF
λ / r0
λ / r0
λ / D
λ / D
r0 / λ
D / λ
r0 / λ
D / λ
θ-1
θ-1

## Slide 63: Next time: Derive r0 and all the good things that come from knowing r0
Define r0 as the telescope diameter where the optical transfer functions of the telescope and atmosphere are equal
Use r0 to derive relevant timescales of turbulence
Use r0 to derive “Isoplanatic Angle”:
  AO performance degrades as astronomical targets get farther from guide star