## Slide 1: Lecture 8: Wavefront Sensing
Claire Max
Astro 289C, UCSC
February 4, 2020

## Slide 2: Outline of lecture
General discussion: Types of wavefront sensors
Three types in more detail:
  Shack-Hartmann wavefront sensors
  Curvature sensing
  Pyramid sensing

## Slide 3: At longer wavelengths, one can measure phase directly
FM radios, radar, radio interferometers like the VLA, ALMA
All work on a narrow-band signal that gets mixed with a very precise “intermediate frequency” from a local oscillator. “Heterodyne” measurement.
Very hard to do this at visible and near-infrared wavelengths
  Could use a laser as the intermediate frequency, but would need tiny bandwidth of visible or IR light
Thanks to Laird Close’s lectures for making this point

## Slide 4: At visible and near-IR wavelengths, measure phase via intensity variations
Difference between various wavefront sensor schemes is the way in which phase differences are turned into intensity differences
General box diagram:
Guide
star
Turbulence
Telescope
Optics
Detector of Intensity
Recon-structor
Wavefront sensor
Transforms aberrations into intensity variations
Computer

## Slide 5: How to use intensity to measure phase?
Irradiance transport equation: A is complex field amplitude, z is propagation direction. (Teague, 1982, JOSA 72, 1199)
Follow I (x,y,z) as it propagates along the z axis (paraxial ray approximation: small angle w.r.t. z)
Wavefront tilt: Hartmann and Pyramid sensors
Wavefront curvature: Curvature Sensors

## Slide 6: Types of wavefront sensors
“Direct” in pupil plane: split pupil up into subapertures in some way, then use intensity in each subaperture to deduce phase of wavefront.
  Slope sensing: Shack-Hartmann, Pyramid sensing
  Curvature sensing
“Indirect” in focal plane: wavefront properties are deduced from whole-aperture intensity measurements made at or near the focal plane. Iterative methods –calculations take longer to do.
  Image sharpening
  Phase diversity, phase retrieval, Gerchberg-Saxton (these are used, for example, in JWST)
  Usually used to measure nearly static aberrations

## Slide 7: How to reconstruct wavefront from measurements of local “tilt”

## Slide 8: Shack-Hartmann wavefront sensor concept - measure subaperture tilts
CCD
CCD
f
Pupil plane
Image plane
Credit:
A. Tokovinin

## Slide 9: Example: Shack-Hartmann Wavefront Signals
Credit: Cyril Cavadore

## Slide 10: Displacement of centroids
Definition of centroid
Centroid is intensity weighted
Each arrow represents an offset proportional to its length
Credit: Cyril Cavador

## Slide 11: Notional Shack-Hartmann Sensor spots
Credit: Boston Micromachines

## Slide 12: Displacement of Hartmann Spots

## Slide 13: Quantitative description of Shack-Hartmann operation
Relation between displacement of Hartmann spots and slope of wavefront:
  where k = 2π / λ , Δx is the lateral displacement of a subaperture image, M is the (de)magnification of the system, f is the focal length of the lenslets in front of the Shack-Hartmann sensor

## Slide 14
Credit: Marcos van Dam

## Slide 15
Shack-Hartmann Spots
Wavefront shape
Credit: Thorlabs

## Slide 16: How to measure distance a spot has moved on CCD? “Quad cell formula”
b

## Slide 17: Disadvantage: “gain” depends on spot size b which can vary during the night
b
Slope = 2/b

## Slide 18: Question
What might happen if the displacement of the spot is > radius of spot? Why?
?
?

## Slide 19: Signal becomes nonlinear and saturates for large angular deviations
b
“Rollover” corresponds to spot being entirely outside of 2 quadrants

## Slide 20: Measurement error from Shack-Hartmann sensing
Measurement error depends on size of spot as seen in a subaperture, θb , wavelength λ , subaperture size d, and signal-to-noise ratio SNR:
      (Hardy equation 5.16)

## Slide 21: Order of magnitude, for r0 ~ d
If we want the wavefront error to be < λ/20, we need

## Slide 22: General expression for signal to noise ratio of a pixelated detector
S = flux of detected photoelectrons / subap npix = number of detector pixels per subaperture
R = read noise in electrons per pixel
The signal to noise ratio in a subaperture for fast CCD cameras is dominated by read noise, and
See McLean, “Electronic Imaging in Astronomy”, Wiley

## Slide 23: Trade-off between dynamic range and sensitivity of Shack-Hartmann WFS
If spot is diffraction limited in a subaperture d, linear range of quad cell (2x2 pixels) is limited to ± λref/2d.
Can increase dynamic range by enlarging the spot (e.g. by defocusing it).
But uncertainty in calculating centroid ∝ width x Nph1/2 so centroid calculation will be less accurate.
Alternative: use more than 2x2 pixels per subaperture. Decreases SNR if read noise per pixel is large (spreading given amount of light over more pixels, hence more read noise).
Linear range

## Slide 24: Correlating Shack-Hartmann wavefront sensor uses images in each subaperture
Solar adaptive optics: Rimmele and Marino, Solar Physics Living Reviews
Cross-correlation is used to track low contrast granulation
Left: Subaperture images, Right: cross-correlation functions
Notes: Link is wrong

## Slide 25: Brand new result: video of Sun from DKIST telescope, with AO

## Slide 26: Zoomed-in Version

## Slide 27: Review of Shack-Hartmann geometry
f
Pupil plane
Image plane

## Slide 28: Pyramid sensor reverses order of operations in a Shack-Hartmann sensor

## Slide 29: A Pyramid WFS
Stellar image is placed on the tip of a four sided pyramid --- Creates four beams.
Intermediate optics form pupil images from the four beams.
Credit: Sebastian Egner
Image Plane
Pupil Plane

## Slide 30: Pyramid for the William Herschel Telescope’s AO system

## Slide 31: Typical intensity patterns for a Pyramid Sensor
Credit: Charlotte Bond

## Slide 32: Aspects of Pyramid Sensors
More sensitive to low order modes.
  Good match to atmosphere.
  A change in sampling can easily be carried out via binning of CCD.
Pyramid Based Systems
LBT
Magellan
Subaru SCexAO
Keck IR Pyramid Sensor
Credit: Phil Hinz

## Slide 33
Credit: Marcos van Dam

## Slide 34: Potential advantages of pyramid wavefront sensors
Wavefront measurement error can be much lower
  Shack-Hartmann: size of spot limited to λ / d, where d is size of a sub-aperture and usually d ~ r0
  Pyramid: size of spot can be as small as λ / D, where D is size of whole telescope. So spot can be D/r0 = 20 - 100 times smaller than for Shack-Hartmann
  Measurement error (e.g. centroiding) is proportional to spot size/SNR. Smaller spot = lower error.
Avoids bad effects of charge diffusion in CCDs
  Fuzzes out edges of pixels.
  Pyramid doesn’t mind as much as S-H.

## Slide 35: Potential pyramid sensor advantages, continued
Linear response over a larger dynamic range
Naturally filters out high spatial frequency information that you can’t correct anyway

## Slide 36
Credit: Phil Hinz

## Slide 37: Curvature wavefront sensing
F. Roddier, Applied Optics, 27, 1223- 1225, 1998
Laplacian (curvature)
Normal derivative at boundary
More intense
Less intense

## Slide 38: Wavefront sensor lenslet shapes are different for edge, middle of pupil
Example: This is what wavefront tilt (which produces image motion) looks like on a curvature wavefront sensor
  Constant I on inside
  Excess I on right edge
  Deficit on left edge
Lenslet array

## Slide 39: Simulation of curvature sensor response
Wavefront: pure tilt
Curvature sensor signal
Credit: G. Chanan

## Slide 40: Curvature sensor signal for astigmatism
Credit: G. Chanan

## Slide 41: Practical implementation of curvature sensing
Use oscillating membrane mirror (2 kHz!) to vibrate rapidly between I+ and I- extrafocal positions
Measure intensity in each subaperture with an “avalanche photodiode” (only need one per subaperture!)
  Detects individual photons, no read noise, QE ~ 60%
  Can read out very fast with no noise penalty
More intense
Less intense

## Slide 42: Measurement error from curvature sensing
Error of a single set of measurements is determined by photon statistics, since detector has NO read noise!
  where d = subaperture diameter and Nph is no. of photoelectrons per subaperture per sample period
Error propagation when the wavefront is reconstructed numerically using a computer scales poorly with no. of subapertures N:
  (Error)curvature ∝ N, whereas (Error)Shack-Hartmann ∝ log N

## Slide 43: Advantages and disadvantages of curvature sensing
Advantages:
  Lower noise ⇒ can use fainter guide stars than S-H
  Fast readout ⇒ can run AO system faster
  Can adjust amplitude of membrane mirror excursion as “seeing” conditions change. Affects sensitivity.
  Well matched to bimorph deformable mirror (both solve Laplace’s equation), so less computation.
  Curvature systems appear to be less expensive.
Disadvantages:
  Avalanche photodiodes can fail with too much light
  Hard to use a large number of avalanche photodiodes.
  BUT – recently available in arrays
  Doesn’t scale well to large numbers of subapertures

## Slide 44: Summary of main points
Wavefront sensors in common use for astronomy measure intensity variations, deduce phase. Complementary.
  Shack-Hartmann
  Curvature sensors
Curvature systems: cheaper, fewer degrees of freedom, scale more poorly to high no. of degrees of freedom, but can use fainter guide stars
Shack-Hartmann systems excel at very large no. of degrees of freedom
Most recent addition: pyramid sensors
  Very successful for faint natural guide stars, low modes